## Slide 1
Mike Sobolewski PJIIT
Scott Burton American Optimization LLC
Ray Kolonay US Air Force Research Lab
Multi-Fidelity Analysis in SORCER
20th ISPE International Conference on Concurrent Engineering
RMIT University
Melbourne, Australia
2-6 Sept, 2013

## Slide 2
Typical Target Application
Efficient Supersonic Configuration
Baseline configuration and performance data from previous STAV and CESTA studies
Requirements:
Range = 4000 nmi
Payload = 5-10 % weight fraction
Maneuver Loads at Cruise – 2.5 g
Cruise speed: Mach 2.0
Cruise L/D: 8.5-9
Level 1 Flying Qualities

## Slide 3: Merging Conceptual and Preliminary Design
Modeling for Design
Analysis for Design
Dialable “Appropriate” Fidelity with UQ
Design Space Exploration
10s configuration
3
Get more (and Better) Information … and get it Earlier
Conceptual Design Studies
Technology
Suite
1000s configurations
Prototype
Experimental
Validation
Methods Application &
Technology Validation
My Presentations
Dr. Burton’s Presentation

## Slide 4
Geographic Location B
Geographic Location A
Geographic Location C
.
.
.
.
.
.
New Process Steps (BCA):
Increase Disciplines & Coupling
Increase Fidelity
Leverage All Compute Resources
Design Process Vision
Physics Based Distributed Collaborative Design
Dialable Fidelity
Empirical
Linear Potential
Euler
NS

## Slide 5: Multi-Fidelity Analysis
For Example - Induced Drag
- Closed form (high Aspect Ratio assumption)
- Treftz-Plane analysis
- Force integration
- Various Surrogates to the above
The same engineering quantity can be computed in many different fashions.
- Analytic expressions
- Historical databases/empirical relations
- Solutions to various levels of DE & PDE
- Surrogates to DE & PDE solutions
…
Analyst/Designer will need access to these different levels of fidelity depending on;
- Task at hand(Design Space Exploration, Validation etc..)
- Flight Condition
- Configuration being developed
The Computational Framework Needs to Support this Multi-Fidelity

## Slide 6: Desired API
Anywhere on the network the enduser/developer should be able to do the following;
  Var.getValue(method of Calculation)
  Var.getGradient(method of Calculation)
Var is the enigneering quantity to be computed – Induced Drag for example
method of calculation is the fidelity level.
Use of Var anywhere else should not require changes if fidelity changes

## Slide 7: SORCER Vars
Mathematics
  Independent variables
  Functions
  Composite functions
Demand-driven
Multi-fidelity
Objects in Vars
  Evaluator
  Filter
  Persister
Var: y1v
evaluator reference
y1v value
evaluator value
ExertionEvaluator
Task
Context
Signature
evaluator value
ExertionEvaluator
Task
Context
Signature
evaluator value
ExertionEvaluator
Task
Context
Signature
evaluator value
ExertionEvaluator
Task
Context
Signature
evaluator value
multi-fidelity

## Slide 8: SORCER Evaluators
object to perform calculations
ExertionEvaluator
  Uses remote services
  Requires Task object
    Service type
    Service op
    Provider name (optional)
    Context (service op argument)
ExpressionEvaluator
MethodEvaluator
…
provider name
service ops
Engineering Air Vehicle Provider
(AirVehicleInterface)
doMstcGeomService
executeAwave
service type
ExertionEvaluator
Task
Context
Signature
evaluator value
provider name
(optional)
service op
service type
Notes: Evaluators are used in SORCER Vars to create mathematical functions…

## Slide 9
Elementary Exertion
Composite Exertion
Engineering Example
All are Objects
Exertion Evaluators

## Slide 10
SORCER Filter
  Operates on value returned from evaluator
  Reduces or transforms
SORCER Persisters
  Operates on value returned from filter
  Sets value
    Writes file
    Passes to object
file
Var: y1
filter
evaluator reference
y1 value
evaluator value
persister
ExertionEvaluator
Task
Context
Signature
evaluator value
file
Var: y2
filter
evaluator reference
y2 value
evaluator value
persister
SORCER Vars
Notes: Filters may be chained together to for a filter pipeline.

## Slide 11
dy1e1dx1
dy1e1dx2
dy1e1dx3
dy1e1dx3
y1 | y2 | y3
y1e1 | y1e2
dy1e1dx1
dy1e1dx2
dy1e1dx3
dy1e1dx4
Variables
Evaluators
Variables
Multidisciplinary
Multi-fidelity
…
Drag via N-S Calc.
Drag via Surrogate Calc.
dy1e1dx1e1 | dy1e1dx1e2
…
dy1e2dx1e1 | dy1e2dx1e2
…
dy1e1dx4e1 | dy1e1dx4e2
…
dy1e2dx4e1 | dy1e2dx4e2
…
Functions of Functions
y1e1g1
y1e1g2
Gradient
Differentiator
Var Structure

## Slide 12: SORCER Models
Collection of vars
May be published as a provider
Single model query
  Set Xs, get Ys
  Behaves like shared memory
Table model query
  Rows of Xs
  Creates new isolated model objects
  Executes in parallel
OptimizationModel: model1
Var: y1v
filter
Var: x1v
Var: y2v

## Slide 13: SORCER Provider
Java object in a JVM on a computer
Provide Java methods called service operations to remote users over a network
Implements a Java interface called a service type
AirVehicleInterface
Context doMstcGeomService(Context ctx);
Context executeAwave(Context ctx);
service type
service ops
provider object
provider name
service ops
JVM Process
Engineering Air Vehicle Provider
(AirVehicleInterface)
doMstcGeomService
executeAwave
service type
Notes: Users don’t need to know where a provider is, nor it’s name (no host, port, or name required)

## Slide 14: SORCER Services
Typically wrap engineering analysis executables
Java service code may augment native executables
Communication
  File-based
  Java Native Interface (JNI)
  Java Native Access (JNA)
Engineering Air Vehicle Provider
doMstcGeomService
executeAwave
awave.exe
executes
reads
writes
output file
reads
writes
input file
Notes: SORCER services are used by clients via the Evaluator object.

## Slide 15: Model Example: Induced Drag Optimization

## Slide 16: Trefftz-Plane Induced Drag
(Kutta-Joukowski theorem)

## Slide 17: Optimization Problem
At Transonic Mach #’s Computation of Lpus requires Euler Solution

## Slide 18: Fidelities for and
Linear Potential Method(LPM) | X | FFD | X | FFD
Standard One Point Approximation with LPM | X | Constant | X | Constant
Modified One Point Approximation with LPM |  |  | X | Semi-Analytic
Kriging with LPM |  |  | X | 
Euler Method (EM) | X | FFD | X | FFD
Standard One Point Approximation with EM | X | Constant | X | FFD
Modified One Point Approximation with EM |  |  | X | Semi-Analytic
Kriging with EM |  |  | X | 
Fidelity

## Slide 19: SORCER Model Construction
Constructing a Model Consists of Two Steps
  Model Definition (Skeleton)
    Defines the model Variables (independent, dependent, parameters, objectives, constraints.
    Defines the Variable Realizations, Evaluations, and Differentiation
  Model Configuration (Muscle)
    Develops the evaluators and filters for all variables and derivative variables.
Models can be created programmatically with or without
Operators (Functional Programming)

## Slide 20: Engineering – Induced Drag Optimization Model Definition
OptimizationModel omodel = optimizationModel("Induced Drag”
designVars(vars(loop("i",1,20),"beta$i$", 0.2, -10.0, 10.0)),
linkedVars(names(loop("i",21,40),"betal$i$")),
designVars(var("alpha", 5.0, -5.0, 10.0)),
designVars(var("mach",0.75, 0.7, 0.85)),
designVars(var("q", 5.0, 4.5, 10.0)),
designVars(var("static pressure", -1., -1., 14.696))
parameter("gamma", 1.4),
dependentVar("DI",
realization(
evaluation("LinearPotentialExact", "DIAstrosExacte",
differentiation(wrt(names(loop("i",1,40),"Lpus$i$"),"q"), gradient("DIAstrosExacteg1"))),
evaluation("LinearPotentialSOA", "DIAstrosSOAe",
differentiation(wrt(names(loop("i",1,40),"Lpus$i$"),"q"), gradient("DIAstrosSOAeg1"))),
evaluation("LinearPotentialMOA", "DIAstrosMOAe",
differentiation(wrt(names(loop("i",1,40),"Lpus$i$"),"q"), gradient("DIAstrosMOAeg1"))),
evaluation("LinearPotentialKriging", "DIAstrosKriginge",
differentiation(wrt(names(loop("i",1,40),"Lpus$i$"), "q"), gradient("DIAstrosKrigingeg1"))),
evaluation("EulerExact", "DIAvusExacte",
differentiation(wrt(names(loop("i",1,40),"Lpus$i$"),"static pressure", "mach"), gradient("DIAvusExacteg1"))),
evaluation("EulerSOA", "DIAvusSOAe",
differentiation(wrt(names(loop("i",1,40),"Lpus$i$"),"static pressure", "mach"), gradient("DIAvusSOAeg1"))),
evaluation("EulerMOA", "DIAvusMOAe",
differentiation(wrt(names(loop("i",1,40),"Lpus$i$"),"static pressure", "mach"), gradient("DIAvusMOAeg1"))),
evaluation("EulerKriging", "DIAvusKriginge",
differentiation(wrt(names(loop("i",1,40),"Lpus$i$"), "static pressure", "mach"), gradient("DIAvusKrigingeg1")))
)
),

## Slide 21: Engineering – Induced Drag Optimization Model Definition
dependentVars(loop("i",1,40),"Lpus$i$",
realization(
evaluation(”LinearPotentialExact", "LpusAstrosExacte",
differentiation(wrt(names(loop("k",1,20),"beta$k$"), "alpha", "q"), gradient("Lpus$i$AstrosExacteg1"))),
evaluation(”LinearPotentialSOA","Lpus$i$AstrosSOAe",
differentiation(wrt(names(loop("k",1,20),"beta$k$"), "alpha", "q"), gradient("Lpus$i$AstrosSOAeg1"))),
evaluation(”EulerExact", "LpusAvusExacte",
differentiation(wrt(names(loop("k",1,20),"beta$k$"), "alpha", "static pressure", "mach"), gradient("Lpus$i$AvusExacteg1"))),
evaluation(”EulerSOA","Lpus$i$AvusSOAe",
differentiation(wrt(names(loop("k",1,20),"beta$k$"), "alpha", "static pressure", "mach"), gradient("Lpus$i$AvusSOAeg1")))
)
),
objectiveVars(var("DIo", "DI", Target.min )),
constraintVars(var("LTc", "LT", Relation.eq, 1000.0))

## Slide 22: Configuring the Variables in the Model
Consider the necessary Evaluators for
Exertion Evaluator Euler - Avus
Configure the Evaluators
EF
OF
LF
Method Evaluator “evaluateIDrag”
Induced Drag
Configure the Evaluators

## Slide 23: Simple SORCER Network Configuration for Example
SORCER Enables Seamless Access to All Methods, Models, Data, and Computing Resources
AVUS Provider
Euler LPUS Calculations
NMEDA – Linux Beau Wolf Cluster
Astros (LPM) LPUS Calculations
Optimization Model – SOA, MOA, FFD
Calculations
Gladius – Linux Desktop
Client
Sobolewski, M., Kolonay, R “Federated Grid Computing with Interactive Service-oriented Programming,” International Journal of Concurrent Engineering: Research & Applications, Vol. 14, No 1 2006 pp. 55-66
MacDNA – MACBookPro

## Slide 24: Model/Variable Use
Once the Variables & Model are configured (see paper for details)
Anywhere on the network the following API will work.
API Example 1:
// set “beta1” to 5.0
Omodel.getVar(“beta1”).setValue(5.0);
Omodel.getVar(“Lpus1”).getValue();
Behavior - kick off Lpus calculation (run the Avus Task) due to dependency of “Lpus1” on “beta1” (observe – observable pattern)
Omodel.getVar(“Lpusi”).getValue();
Behavior – Will NOT kick off Lpus calculation (run the Avus Task) since all “Lpusi” use the same evaluator(only different filters) and none of its dependencies have changed their values.

## Slide 25: Model/Variable Use (Cont)
Omodel.getVar(“iDrag”).getDerivative(“Euler Exact”, “DIAvusExacteg1”, “beta1”, “beta2”, “beta15”)
Behavior - kicks off chain rule differentiation for
by FFD Evaluators run the Avus Task – Note only 4 Avus runs done )
done analytically by a Method Evaluator

## Slide 26: Concluding Remarks
Very Brief Overview of SORCER that supports Large Scale Distributed MDMFMS-AO-UQ
Developed Computational Environment (Variable, Filter, Evaluator and Model) to support Functions of Functions and Mult-Fideltiy Analysis/Sensitives.
Anywhere on the network
    Var.setValue(x)
    Var.getValue(method of Calculation)
    Var.getGradient(method of Calculation)
No need to change other code dependent on Drag

## Slide 27
Questions?

## Slide 28: SORCER Model
Models – consists of a collection of Variables.
  Current available models – ResponseModel(including sensitivities) , ParametricModel,, OptimizationModel
Variables - can be dependent on other Variables enabling distributed functional programming. Variables can have multiple evaluators enabling multi-fidelity calculations for a specific variable’s value.
  Current Variable Types - DESIGN, RESPONSE, DERIVATIVE, GRADIENT, RANDOM, BOUNDED, LINKED, PARAMTER
Evaluators – are used to determine the value of variables and their partial derivatives(chain rule works) with respect to their dependencies (Variables).
  Current Evaluator Types – ModelEvaluator, ExertionEvaluator, ExpressionEvaluator, GroovyEvaluator, JepEvaluator, MethodEvaluator
Filters - are used to map the results of Evaluators to Variable Values. Think unix shell piping. Filters can be concatenated n times.
  Current Filter Types – BasicFileFilter, ContextFilter, FileFilter, GrepFilter, ListFilter, MapFilter, ObjetFilter, PatternFilter, TextFilter
All are Objects

## Slide 29: Rosen-Suzuki Functions
Model Definition
ResponseModel rm = ResponseModel(“Rosen-Suzuki Model",
designVars("x", 4), // creates 4 real design variables x1-x4
responseVars("f"), // creates 1 response variable f
responseVars("g", 3) //creates 3 response variables g1-g3
);

## Slide 30: Rosen-Suzuki Functions
Model Configuration
// configure response vars
Evaluator fe = evaluator("fe", "x1^2-5.0*x1+x2^2-5.0*x2+2.0*x3^2-21.0*x3+x4^2+7.0*x4+50.0");
rm.setResponseEvaluator("f", fe);
fe.addArgs( om.getDesignVars("x1", "x2", "x3", "x4"));
Evaluator g1e = evaluator("g1e", "x1^2+x1+x2^2-x2+x3^2+x3+x4^2-x4-8.0");
rm.setResponseEvaluator("g1", g1e);
g1e.addArgs(om.getDesignVars("x1", "x2", "x3", "x4"));
Evaluator g2e = evaluator("g2e", "x1^2-x1+2.0*x2^2+x3^2+2.0*x4^2-x4-10.0");
rm.setResponseEvaluator("g2", g2e);
g2e.addArgs(om.getDesignVars("x1", "x2", "x3", "x4"));
Evaluator g3e = evaluator("g3e", "2.0*x1^2+2.0*x1+x2^2-x2+x3^2-x4-5.0");
rm.setResponseEvaluator("g3", g3e);
g3e.addArgs(om.getDesignVars("x1", "x2", "x3", "x4"));

## Slide 31: Rosen-Suzuki Functions
Model Use
// you can set the value of the independent variables
rm.setDesignVarValues(set("x1", 2.0), set("x2", 3.0), set("x3", 4.0), set("x4", 200.0));
// get the values of the responses for the new x values
rm.getRepsonses();
Data Table [x1,x2,x3,x4, f, g1,g2,g3]
[2.0, 3.0, 4.0, 5.0, 46., 44.0, 71.0, 24.0]
// additional examples of using the api
Var x4 = rm.getDesignVar("x4");
logger.info("\n\nx4 value: " + x4.getValue());
x4 value: 5.0
// examine the responseVar f
Var f = rm.getResponseVar("f");
ExpressionEvaluator ee = (ExpressionEvaluator) f.getEvaluator();
logger.info("\n\nexpression:\n" + ee.getName() + "/" + ee.getExpression());
fe/x1^2-5.0*x1+x2^2-5.0*x2+2.0*x3^2-21.0*x3+x4^2+7.0*x4+50.0
logger.info("\n\nresponse:\n" + ee.getName() + "/" + f.getValue());
fe/46.0

## Slide 32: Rosen-Suzuki Function Optimization Definition
Minimize
Subject to:

## Slide 33: Objective Function, Constraints and Sensitivities
Objective Sensitivities:
Constraints Sensitivities:

## Slide 34: Rosen-Suzuki Function Optimization
Optimization Model Definition
OptimizationModel om = optimizationModel("DesignExploration Model",
designVars(vars(loop(4), "x", 0.0,-100., 100.)),
responseVars("f"),
responseVars("g”,3),
objectiveVars(var("fo", "f", Target.min )),
constraintVars(var("g1c", "g1", Relation.lt, 0.0),
var("g2c", "g2", Relation.lt, 0.0),
var("g3c","g3", Relation.lt, 0.0)))
);

## Slide 35: Rosen-Suzuki Function Optimization
Optimization Model Configuration
Sensitivity Evaluators for the Objective
Evaluator dfedx1e1 = evaluator("dfedx1e1", "2.0*x1-5.0",args(om.getDesignVars("x1")));
Evaluator dfedx2e1 = evaluator("dfedx2e1", "2.0*x2-5.0",args(om.getDesignVars("x2")));
Evaluator dfedx3e1 = evaluator("dfedx3e1", "4.0*x3-21.0",args(om.getDesignVars("x3")));
Evaluator dfedx4e1 = evaluator("dfedx4e1", "2.0*x4+7.0",args(om.getDesignVars("x4")));
List<Evaluator> feg1 = list(dfedx1e1, dfedx2e1, dfedx3e1, dfedx4e1);
om.setGradientEvaluators("f", "fe", "feg1", feg1);

## Slide 36: Rosen-Suzuki Function Optimization
Optimization Model Configuration
Sensitivity Evaluators for the Constraints
Evaluator dg1edx1e1 = evaluator("dg1edx1e1", "2.0*x1+1",args(om.getDesignVars("x1")));
Evaluator dg1edx2e1 = evaluator("dg1edx2e1", "2.0*x2-1.0",args(om.getDesignVars("x2")));
Evaluator dg1edx3e1 = evaluator("dg1edx3e1", "2.0*x3+1.0",args(om.getDesignVars("x3")));
Evaluator dg1edx4e1 = evaluator("dg1edx4e1", "2.0*x4-1.0",args(om.getDesignVars("x4")));
List<Evaluator> g1eg1 = list(dg1edx1e1, dg1edx2e1, dg1edx3e1, dg1edx4e1);
om.setGradientEvaluators("g1", "g1e", "g1eg1", g1eg1);

## Slide 37: Rosen-Suzuki Function Optimization
Optimization Model Configuration
Sensitivity Evaluators for the Constraints
Evaluator dg2edx1e1 = evaluator("dg2edx1e1", "2.0*x1-1",args(om.getDesignVars("x1")));
Evaluator dg2edx2e1 = evaluator("dg2edx2e1", "4.0*x2",args(om.getDesignVars("x2")));
Evaluator dg2edx3e1 = evaluator("dg2edx3e1", "2.0*x3",args(om.getDesignVars("x3")));
Evaluator dg2edx4e1 = evaluator("dg2edx4e1", "4.0*x4-1.0",args(om.getDesignVars("x4")));
List<Evaluator> g2eg1 = list(dg2edx1e1, dg2edx2e1, dg2edx3e1, dg2edx4e1);
om.setGradientEvaluators("g2", "g2e", "g2eg1", g2eg1);

## Slide 38: Rosen-Suzuki Function Optimization
Optimization Model Configuration
Sensitivity Evaluators for the Constraints
Evaluator dg3edx1e1 = evaluator("dg3edx1e1", "4.0*x1+2.0",args(om.getDesignVars("x1")));
Evaluator dg3edx2e1 = evaluator("dg3edx2e1", "2.0*x2-1.0",args(om.getDesignVars("x2")));
Evaluator dg3edx3e1 = evaluator("dg3edx3e1", "2.0*x3",args(om.getDesignVars("x3")));
Evaluator dg3edx4e1 = evaluator("dg3edx4e1", "-1.0");
List<Evaluator> g3eg1 = list(dg3edx1e1, dg3edx2e1, dg3edx3e1, dg3edx4e1);
om.setGradientEvaluators("g3", "g3e", "g3eg1", g3eg1);

## Slide 40: Rosen-Suzuki Function Optimization
Model
Dispatcher
Optimizer
register
update
Dispatcher#
notify:ModelContext
from model
register search
Optimizer#processContext(SearchContext):SearchContext
Modeling#update(Context):void
Modeling#model(Context):Context
Explorer
Explore Context
Explorer#explore(Context):Context
Exploration
SearchContext
ModelContext

## Slide 41: Explorer Context (Data)
VariableInfo
Objectives Info
Constraints Info
Design Variable Info
Objectives Gradient Info
Constraints Gradient Info
Optimization Strategy
Optimization State
Optimization Signature
Dispatcher Signature
Model Signature
Optimization
Dispatcher
Model
Explorer Context

## Slide 42: Standard One Point Approximation (SOA)
In terms of the induced drag function

## Slide 43: Approximations
Linear Approximations
  (First Order Taylor Series Expansion)

## Slide 44: Inner/Outer Loop Optimization Algorithm
Approximate Analysis
Control Program
Exact Engineering Analysis
Constraint Screening
Sensitivity Analysis
Optimizer
Inner Loop
Approximate Problem Generator
Outer Loop
minutes
to days

## Slide 45: Variable Structure
dy1e1dx1
dy1e1dx2
dy1e1dx3
dy1e1dx3
y1 | y2 | y3
y1e1 | y1e2
dy1e1dx1
dy1e1dx2
dy1e1dx3
dy1e1dx4
Variables
Evaluators
Variables
Multidisciplinary
Multi-fidelity
…
Drag via N-S Calc.
Drag via Surrogate Calc.
dy1e1dx1e1 | dy1e1dx1e2
…
dy1e2dx1e1 | dy1e2dx1e2
…
dy1e1dx4e1 | dy1e1dx4e2
…
dy1e2dx4e1 | dy1e2dx4e2
…
Functions of Functions
y1e1g1
y1e1g2
Gradient
Differentiator

## Slide 46: Model Example: Induced Drag Optimization

## Slide 47: Trefftz-Plane Induced Drag
(Kutta-Joukowski theorem)

## Slide 48: Optimization Problem
At Transonic Mach #’s Computation of Lpus requires Euler Solution

## Slide 49: Fidelities for and
Linear Potential Method(LPM) | X | FFD | X | FFD
Standard One Point Approximation with LPM | X | Constant | X | Constant
Modified One Point Approximation with LPM |  |  | X | Semi-Analytic
Kriging with LPM |  |  | X | 
Euler Method (EM) | X | FFD | X | FFD
Standard One Point Approximation with EM | X | Constant | X | FFD
Modified One Point Approximation with EM |  |  | X | Semi-Analytic
Kriging with EM |  |  | X | 
Fidelity

## Slide 50: SORCER Model Construction
Constructing a Model Consists of Two Steps
  Model Definition (Skeleton)
    Defines the model Variables (independent, dependent, parameters, objectives, constraints.
    Defines the Variable Realizations, Evaluations, and Differentiation
  Model Configuration (Muscle)
    Develops the evaluators and filters for all variables and derivative variables.
Models can be created programmatically with or without
Operators (Functional Programming)

## Slide 51: Engineering – Induced Drag Optimization Model Definition
OptimizationModel omodel = optimizationModel("Induced Drag”
designVars(vars(loop("i",1,20),"beta$i$", 0.2, -10.0, 10.0)),
linkedVars(names(loop("i",21,40),"betal$i$")),
designVars(var("alpha", 5.0, -5.0, 10.0)),
designVars(var("mach",0.75, 0.7, 0.85)),
designVars(var("q", 5.0, 4.5, 10.0)),
designVars(var("static pressure", -1., -1., 14.696))
parameter("gamma", 1.4),
dependentVar("DI",
realization(
evaluation("LinearPotentialExact", "DIAstrosExacte",
differentiation(wrt(names(loop("i",1,40),"Lpus$i$"),"q"), gradient("DIAstrosExacteg1"))),
evaluation("LinearPotentialSOA", "DIAstrosSOAe",
differentiation(wrt(names(loop("i",1,40),"Lpus$i$"),"q"), gradient("DIAstrosSOAeg1"))),
evaluation("LinearPotentialMOA", "DIAstrosMOAe",
differentiation(wrt(names(loop("i",1,40),"Lpus$i$"),"q"), gradient("DIAstrosMOAeg1"))),
evaluation("LinearPotentialKriging", "DIAstrosKriginge",
differentiation(wrt(names(loop("i",1,40),"Lpus$i$"), "q"), gradient("DIAstrosKrigingeg1"))),
evaluation("EulerExact", "DIAvusExacte",
differentiation(wrt(names(loop("i",1,40),"Lpus$i$"),"static pressure", "mach"), gradient("DIAvusExacteg1"))),
evaluation("EulerSOA", "DIAvusSOAe",
differentiation(wrt(names(loop("i",1,40),"Lpus$i$"),"static pressure", "mach"), gradient("DIAvusSOAeg1"))),
evaluation("EulerMOA", "DIAvusMOAe",
differentiation(wrt(names(loop("i",1,40),"Lpus$i$"),"static pressure", "mach"), gradient("DIAvusMOAeg1"))),
evaluation("EulerKriging", "DIAvusKriginge",
differentiation(wrt(names(loop("i",1,40),"Lpus$i$"), "static pressure", "mach"), gradient("DIAvusKrigingeg1")))
)
),

## Slide 52: Engineering – Induced Drag Optimization Model Definition
dependentVars(loop("i",1,40),"Lpus$i$",
realization(
evaluation(”LinearPotentialExact", "LpusAstrosExacte",
differentiation(wrt(names(loop("k",1,20),"beta$k$"), "alpha", "q"), gradient("Lpus$i$AstrosExacteg1"))),
evaluation(”LinearPotentialSOA","Lpus$i$AstrosSOAe",
differentiation(wrt(names(loop("k",1,20),"beta$k$"), "alpha", "q"), gradient("Lpus$i$AstrosSOAeg1"))),
evaluation(”EulerExact", "LpusAvusExacte",
differentiation(wrt(names(loop("k",1,20),"beta$k$"), "alpha", "static pressure", "mach"), gradient("Lpus$i$AvusExacteg1"))),
evaluation(”EulerSOA","Lpus$i$AvusSOAe",
differentiation(wrt(names(loop("k",1,20),"beta$k$"), "alpha", "static pressure", "mach"), gradient("Lpus$i$AvusSOAeg1")))
)
),
objectiveVars(var("DIo", "DI", Target.min )),
constraintVars(var("LTc", "LT", Relation.eq, 1000.0))

## Slide 53: Configuring the Variables in the Model
Consider the necessary Evaluators for
Exertion Evaluator Euler - Avus
Configure the Evaluators
EF
OF
LF
Method Evaluator “evaluateIDrag”
Induced Drag
Configure the Evaluators

## Slide 54: Simple SORCER Network Configuration for Example
SORCER Enables Seamless Access to All Methods, Models, Data, and Computing Resources
AVUS Provider
Euler LPUS Calculations
NMEDA – Linux Beau Wolf Cluster
Astros (LPM) LPUS Calculations
Optimization Model – SOA, MOA, FFD
Calculations
Gladius – Linux Desktop
Client
Sobolewski, M., Kolonay, R “Federated Grid Computing with Interactive Service-oriented Programming,” International Journal of Concurrent Engineering: Research & Applications, Vol. 14, No 1 2006 pp. 55-66
MacDNA – MACBookPro

## Slide 55: Model/Variable Use
Once the Variables & Model are configured (see paper for details)
Anywhere on the network the following API will work.
API Example 1:
// set “beta1” to 5.0
Omodel.getVar(“beta1”).setValue(5.0);
Omodel.getVar(“Lpus1”).getValue();
Behavior - kick off Lpus calculation (run the Avus Task) due to dependency of “Lpus1” on “beta1” (observe – observable pattern)
Omodel.getVar(“Lpusi”).getValue();
Behavior – Will NOT kick off Lpus calculation (run the Avus Task) since all “Lpusi” use the same evaluator(only different filters) and none of its dependencies have changed their values.

## Slide 56: Model/Variable Use
API Example 2:
// set “beta12” to -8.0
Omodel.getVar(“beta12”).setValue(-8.0);
Omodel.getVar(“DI”).getValue();
Behavior - kick off Lpus calculation (run the Avus Task) due to implicit dependency of “DI” on “beta12” (observe – observable pattern)

## Slide 57: Model/Variable Use (Cont)
Omodel.getVar(“iDrag”).getDerivative(“Euler Exact”, “DIAvusExacteg1”, “beta1”, “beta2”, “beta15”)
Behavior - kicks off chain rule differentiation for
by FFD Evaluators run the Avus Task – Note only 7 Avus runs done )
done analytically by a Method Evaluator

## Slide 58: Concluding Remarks
Very Brief Overview of SORCER that supports Large Scale Distributed MDMFMS-AO-UQ (Many references in the paper for detail)
Developed Computational Environment (Variable, Filter, Evaluator and Model) to support Functions of Functions and Mult-Fideltiy Analysis/Sensitives.
Anywhere on the network
    Var.setValue(x)
    Var.getValue(method of Calculation)
    Var.getGradient(method of Calculation)

## Slide 59: Rosen-Suzuki Function Optimization
ExploreContext exploreContext = new ExploreContext("Rosen-Suzuki");
VarInfoList designInfo = varsInfo(varInfo("x1", 1.0), varInfo("x2", 1.0), varInfo("x3", 1.0), varInfo("x4", 1.0));
exploreContext.setDesignVarsInfo(designInfo);
exploreContext.setObjectivesInfo(null);
exploreContext.setObjectivesGradientInfo(null);
exploreContext.setConstraintsInfo(null);
exploreContext.setConstraintsGradientInfo(null);
ConminStrategy cmnStrategy=new ConminStrategy(new File(System.getProperty("conmin.strategy.file")));
exploreContext.setOptimizerStrategy(cmnStrategy);
//exploreContext.setOptimizerState(cmnState); // state initialized in Dispatcher after first Model update
// specify the Model
exploreContext.setModelSignature(signature("createModel", RosenSuzukiModelCreator.class, Type.INTRAPROCESS));
//specify the Optimizer
exploreContext.setOptimizerSignature(signature(null, ConminOptimizerJNA.class, Type.INTRAPROCESS));
// specify the explorer dispatched
exploreContext.setDispatcherSignature(signature(null, RosenSuzukiDispatcher.class, Type.INTRAPROCESS));
Explorer Context

## Slide 60: Rosen-Suzuki Function Optimization
Explorer Execution
outContext = (ExploreContext)explorer.explore(exploreContext);
********* CONMIN STATE **************
CONMIN Iteration # = 29
Objective Fuction fo = 6.00260795945281
Design Variable Values
x1 = 2.5802964087086235E-4 x2 = 0.9995594642481355 x3 = 2.000313835134211 x4 = -0.9986692050113675
Constraint Values
g1c = -0.002603585246998996 g2c = -1.0074147118087602 g3c = 4.948009193483927E-7
T
Termination Criterion
ABS(OBJ(I)-OBJ(I-1)) LESS THAN DABFUN = 5.0E-5 FOR 3 ITERATIONS
Evaluation Statistics
Number of Objective Evaluations = 88
Number of Constraint Evaluations = 88
Number of Objective Gradient Evaluations = 29
Number of Constraint Gradient Evaluations = 29
Analytic Optimum Results
fo = 6.0
X1=0.0, x2=1.0, x3=2.0, x4=-1.0
g1c=0.0, g2c=-1.0, g3c=0.0

## Slide 61: Rosen-Suzuki Function Optimization
DEMO

## Slide 62: MSTC SORCER Applications to Date
Hi-Fidelity Aeroelastic Analysis
  Euler (AVUS), FEM (MSCNASTRAN), MDICE
Hi-Fidelity Induced Drag minimization
  Euler (AVUS), Optimization (CONMIN, MATLAB)
2-D large amplitude airfoil motion trajectory Optimization
  Unsteady Vortex Lattice Method (in-house UVLM), Opti (DOT)
Shape and sizing aeroelastic optimization
  Euler (AVUS), FEM (MSCNASTRAN), MDICE, Opti (DOT) FD sensitivities
Small UAV MDO (aero, structures, acoustics, controls)
Efficient Supersonic Air Vehicle Design (ESAV)
Demonstrated tight integration with C, C++, and FORTRAN using JNA (can make direct calls to any shared object)
Network configuration
  Linux workstations
  Linux cluster(2), Mac cluster(1)
  SGI Irix
  Windows
  Mac Desktop
  Mac laptop

## Slide 63: Exertion
Elementary Exertion
Composite Exertion
Job
.
.
.
Job
Engineering Example
All are Objects

## Slide 64
Questions?

## Slide 65: Induced Drag Optimization Motivation
Long duration on station
Large changes of over the mission

## Slide 66: A Solution
Utilize conformal control surfaces to enhance laminar flow, minimize the Drag
FlexSys Inc.
Adaptive Compliant Wing

## Slide 67: Modeling Conformal Control Surfaces

## Slide 68: Trefftz-Plane Induced Drag With Euler Aerodynamics
(Kutta-Joukowski theorem)

## Slide 69: Optimization Problem
At Transonic Mach #’s Computation of Lpus requires Euler Solution

## Slide 70
Evaluators for Induced Drag and Sensitivities
Standard One Point Approximation (SOA) – Perform Euler solutions
Exact – Perform Euler solution for
By FD Euler Solutions
Kriging – Perform Euler solutions (hundreds) for Kriging Model
Modified One Point Approximation (MOA) – Perform Euler solution

## Slide 71: Induced Drag Optimization Model
OptimizationModel omodel = optimizationModel("Induced Drag",
designVars(vars(loop("i",1,20),"beta$i$", 0.0, -10.0, 10.0)),
linkedVars(names(loop("i",21,40),"betal$i$")),
designVars(var("alpha", 5.0, -5.0, 10.0)),
designVars("mach", "gamma", "pstatic"),
responseVars(var("DI",
realization(
evaluation("DIExacte",
differentiation(wrt(names(loop("i",1,20),"beta$i$"), "alpha","q"), gradient("DIExacteg1"))),
evaluation("DISOAe",
differentiation(wrt(names(loop("i",1,20),"beta$i$"), "alpha","q"), gradient("DISOAeg1"))),
evaluation("DIMOAe",
differentiation(wrt(names(loop("i",1,20),"beta$i$"), "alpha","q"), gradient("DIMOAeg1"))),
evaluation("DIKrige",
differentiation(wrt(names(loop("i",1,20),"beta$i$"), "alpha","q"), gradient("DIKrigeg1")))))),
responseVars(var("LT",
realization(
evaluation("LTExacte",
differentiation(wrt(names(loop("i",1,20),"beta$i$"), "alpha","q"), gradient("LTExacteg1"))),
evaluation("LTSOAe",
differentiation(wrt(names(loop("i",1,20),"beta$i$"), "alpha","q"), gradient("LTSOAeg1"))),
evaluation("LTMOAe",
differentiation(wrt(names(loop("i",1,20),"beta$i$"), "alpha","q"), gradient("LTMOAeg1")))))),
responseVars(loop("i",1,20),"Lpus$i$",
realization(
evaluation("Lpus$i$Exacte",
differentiation(wrt(names(loop("k",1,20),"beta$k$"), "alpha"), gradient("Lpus$i$Exacteg1"))),
evaluation("Lpus$i$SOAe",
differentiation(wrt(names(loop("k",1,20),"beta$k$"), "alpha"), gradient("Lpus$i$SOAeg1"))))),
responseVars(var("q",
realization(evaluation("qExact", differentiation(wrt("mach","gamma","pstatic"), gradient("qExactg1")))))),
objectiveVars(var("DIo", "DI", Target.min )),
constraintVars(var("LTc", "LT", Relation.eq, 1000.0))
);

## Slide 72: SORCER Network Configuration
SORCER Enables Seamless Access to All Methods, Models, Data, and Computing Resources
AVUS Provider
Euler Drag
Calculations
Coalescence – Linux Beau Wolf Cluster
Numerical Analysis Provider
Gradient Calculations
Nelson – SGI Irix 6.5
DNA – Linux Desk Top
Optimization Provider
Approximations
CONMIN Optimization
Client
Sobolewski, M., Kolonay, R “Federated Grid Computing with Interactive Service-oriented Programming,” International Journal of Concurrent Engineering: Research & Applications, Vol. 14, No 1 2006 pp. 55-66

## Slide 73: Example Case
Goland Wing Planform with a NACA 0006 Airfoil
(Euler Calculations- AVUS (1.5 million cells)
20 Control surfaces @ 20% c
20 ft semi span

## Slide 74: Modified First Order Taylor Series Approximation
 | Value | % Diff
Exact Function | 1.18388E-03 | 0.0%
Tradition First Order Taylor Series Expansion | -4.380E-04 | -137%
Modified First Order Taylor Series Expansion | 1.18708E-03 | 0.27%
Comparison of Traditional and Modified First Order Taylor Series Expansion

## Slide 75: Goland Wing M=0.85, Alpha=5.0
Square Error Objective
versus
Outer Loop Iteration
Iteration #
Square Error
*Lift constraint satisfied to within 0.3%
Spanwise strip
CL per Span
CL per Span Versus Spanwise Strip

## Slide 76: Goland Wing M=0.85, Alpha=5.0
Upper Surface
Upper Surface
Lower Surface
Lower Surface
Cp Initial
Cp Final
0.876
-0.662
degrees

## Slide 77: Shape and Sizing Aeroelastic Optimization
Minimize
Objective Function
Subject to
Inequality
Constraints
Side
Constraints
Ernest Thompson – AFRL/RBSD
- Structural sizes, and planform sweep
Notes: Challenges

## Slide 78: Min weight shape & sizing opti
Mach
q_rev
Ernest Thompson – AFRL/RBSD
- Euler Static Aeroelastic Calculations

## Slide 79: Sorcer network configuration for min weight (shape and sizing)
Gladius
Client
Coalescence
NMEDA
Avus
Avus
Avus
Xserv2
Whittle
Gothmog
RBSDZ0010143
Ernest Thompson – AFRL/RBSD

## Slide 80: Concluding Remarks
Aerospace Vehicle Design requires executing large scale system level MDA/MDO in a heterogenous computing environment
SORCER exposes Sun’s Jini connection Technology to create a Model Oriented Programming (MOP) and computing environment for large scale MDA/MDO
SORCER Functionality
  Create providers and expose them as jini services.
  Exertion Oriented Programming – Ability to orchastrate Services
  Models for analysis, sensitvitities, and design
  VEF – Functional demand driven computations
  Space Computing

## Slide 81: Comments & Questions?

## Slide 82: How to Determine the Compliant Surface Settings?
Approach 1. Indirect – Given a load distribution that is known to minimize drag, determine the control surface settings to obtain the desired load distribution.
Approach 2. Direct - Minimization of drag ( induced drag currently) using the conformal control surface settings.

## Slide 83: Constructing a SORCER Response Model
Construct a Response Model for these functions.
The steps for constructing a Response Model are
1. Define the Model
2. Configure the Model

## Slide 84: Defining a SORCER Response Model
Define the Model –
  Define the Variables declaratively
    VarOperator , Name of Variable(s) and complementary args for ValueType and MathType
  Define the response & linked realizations for the Variables of Type:
    Name of Evaluator(s) and list of Filter(s) for the Variable(s)
  Define the derivative realizations for the Variable Sensitivities
    Name of var, wrt vars, name of vector of evaluators (default FD Evaluators created)
Example: for the Rosen-Suzuki problem –
Variables: Type:DESIGN, Kind: BOUNDED, MathType:[REAL, CONTINUOUS],
ValueType: DOUBLE
Type:RESPONSE, ValueType:DOUBLE
See Appendix C for Details of Model and Variable Definition & Configuration

## Slide 85: Defining a SORCER Response Model
ResponseModel rm = ResponseModel(“Rosen-Suzuki Model",
designVars("x", 4), // creates 4 real design varibles x1-x4
responseVars("f"), // creates 1 response variable f
responseVars("g", 3) //creates 3 response variables g1-g3
);
Code for defining the Repsonse Model
The above creates 4 DESIGN variables with names “x1-x4”, 4 RESPONSE variables “f” and “g1-g3”. There are many defaults used when using the minimum specification above.
The following attributes are default for Type DESIGN – the “xi”
ValueType: DOUBLE
MathType: [REAL, CONTINUOUS]
The following attributes are default for Type RESPONSE – the “f”, “gi”
Kind: [ ]
ValueType: DOUBLE
MathType: [REAL, CONTINUOUS]
The following realizations are default for Type RESPONSE – the “f”, “gi” ( default naming convention – variableNamee.)
realization(“f”, evaluation(“fe”),
realization(“g1”, evaluation(“g1e”),
realization(“g2”, evaluation(“g2e”),
realization(“g3”, evaluation(“g3e”)

## Slide 86: Defining a SORCER Response Model
ResponseModel rm = ResponseModel(“Rosen-Suzuki Model",
designVars(var(“x1”, 2.0, -100., 100.), var(“x2”,3.0,-100., 100.),
var(“x3”,4.0, -100, 100.), var(“x4”,5.0, -100, 100.),
responseVars("f"), // creates 1 response variable f
responseVars("g", 3) //creates 3 response variables g1-g3
realization(“f”, evaluation(“fe”),
realization(“g1”, evaluation(“g1e”),
realization(“g2”, evaluation(“g2e”),
realization(“g3”, evaluation(“g3e”)
);
To specify the initial value and bounds on the DESIGN variables and specify the realizations for the RESPONSE variables:
The ResponseModel class has a very rich API

## Slide 87: Defining a SORCER Response Model
ResponseModel rm = ResponseModel(“Rosen-Suzuki Model",
designVars(vars(loop(“i”,1,20),“x$i$”, 0.0, -10.0, 10.0)),
responseVars("f"), // creates 1 response variable f
responseVars("g", 3) //creates 3 response variables g1-g3
realization(“f”, evaluation(“fe”),
realization(“g1”, evaluation(“g1e”),
realization(“g2”, evaluation(“g2e”),
realization(“g3”, evaluation(“g3e”)
);
If the DesignVariables all have the same initial Values and Bounds:

## Slide 88: Defining a SORCER Response Model
Once the Model is defined it must then be configured
For the RESPONSE Variables to have sensitivities one must include them in the realization of the Variable during the definition of the model.
ResponseModel rm = ResponseModel(“Rosen-Suzuki Model",
designVars(var(“x1”, 2.0, -100., 100.), var(“x2”,3.0,-100., 100.),
var(“x3”,4.0, -100, 100.), var(“x4”,5.0, -100, 100.),
responseVars("f”,
realization((
evaluation(“fe”,
differentiation(wrt(loop(“i”,1,4),”x$i$”), gradient(“feg1”)),
responseVars(names(loop(“i“,1,3),g$i$”),
realization((names(loop(“i“,1,3),g$i$”
evaluation(“g$i$e”,
differentiation(wrt(loop(“k”,1,4),”x$k$”), gradient(“g$i$eg1”))
);

## Slide 89: Configuring a SORCER Response Model
Configuring a Response Model – This requires the definition of the EVALUATORS, and FILTERS (if present) for each of the RESPONSE and LINKED variables. For the Rosen-Suzuki case simple expression evaluators are used. No Filters are required.
// configure response variables
// NOTE: The evaluator names must match the one specified in the realization. There are several was to specify the args.
// configure f
var(model, "f", "fe",evaluator(“fe”, "x1^2-5.0*x1+x2^2-5.0*x2+2.0*x3^2-21.0*x3+x4^2+7.0*x4+50.0”), args(rm.getDesignVars()));
// configure g1
var(model, "g1", "g1e", "x1^2+x1+x2^2-x2+x3^2+x3+x4^2-x4-8.0", args("x1", "x2", "x3", "x4"));
// configure g2
var(model, "g2", "g2e", "x1^2-x1+2.0*x2^2+x3^2+2.0*x4^2-x4-10.0", args("x1", "x2", "x3", "x4"));
// configure g3
var(model, "g3", "g3e", "2.0*x1^2+2.0*x1+x2^2-x2+x3^2-x4-5.0", args("x1", "x2", "x3", "x4"));

## Slide 90: Configuring a SORCER Response Model
Configuring a Response Model (cont) – If you have evaluators for the sensitivity calculations they need to be configured as well.
// configure the sensitivity model
// response f:fe="x1^2-5.0*x1+x2^2-5.0*x2+2.0*x3^2-21.0*x3+x4^2+7.0*x4+50.0"
// derivativeResponse dfdx1:dfedx1 = "2.0*x1-5.0"
// derivativeResponse dfdx2:dfedx2 = "2.0*x2-5.0"
// derivativeResponse dfdx3:dfedx3 = "4.0*x3-21.0"
// derivativeResponse dfdx4:dfedx4 = "2.0*x4+7.0"
Evaluator dfedx1e1 = expression("dfedx1e1", "2.0*x1-5.0",args(sm.getDesignVar("x1")));
Evaluator dfedx2e1 = expression("dfedx2e1", "2.0*x2-5.0",args(sm.getDesignVar("x2")));
Evaluator dfedx3e1 = expression("dfedx3e1", "4.0*x3-21.0",args(sm.getDesignVar("x3")));
Evaluator dfedx4e1 = expression("dfedx4e1", "2.0*x4+7.0",args(sm.getDesignVar("x4")));
List<Evaluator> feg1 = list(dfedx1e1, dfedx2e1, dfedx3e1, dfedx4e1);
sm.setGradientEvaluators("f", "fe", "feg1", feg1);
// response g1:g1e="x1^2+x1+x2^2-x2+x3^2+x3+x4^2-x4-8.0"
// derivativeResponse dg1dx1:dg1edx1 = "2.0*x1+1.0"
// derivativeResponse dg1dx2:dg1edx2 = "2.0*x2-1.0"
// derivativeResponse dg1dx3:dg1edx3 = "2.0*x3+1.0"
// derivativeResponse dg1dx4:dg1edx4 = "2.0*x4-1.0"
Evaluator dg1edx1e1 = expression("dg1edx1e1", "2.0*x1+1",args(sm.getDesignVar("x1")));
Evaluator dg1edx2e1 = expression("dg1edx2e1", "2.0*x21.0",args(sm.getDesignVar("x2")));
Evaluator dg1edx3e1 = expression("dg1edx3e1""2.0*x3+1.0",args(sm.getDesignVar("x3")));
Evaluator dg1edx4e1 = expression("dg1edx4e1", "2.0*x41.0",args(sm.getDesignVar("x4")));
List<Evaluator> g1eg1 = list(dg1edx1e1, dg1edx2e1, dg1edx3e1, dg1edx4e1);
sm.setGradientEvaluators("g1", "g1e", "g1eg1", g1eg1);

## Slide 91: Configuring a SORCER Response Model
// response g2:g2e="x1^2-x1+2.0*x2^2+x3^2+2.0*x4^2-x4-10.0"
// derivativeResponse dg2dx1:dg2edx1 = "2.0*x1-1.0"
// derivativeResponse dg2dx2:dg2edx2 = "4.0*x2"
// derivativeResponse dg2dx3:dg2edx3 = "2.0*x3"
// derivativeResponse dg2dx4:dg2edx4 = "4.0*x4-1.0"
Evaluator dg2edx1e1 = expression("dg2edx1e1", "2.0*x11",args(sm.getDesignVar("x1")));
Evaluator dg2edx2e1 = expression("dg2edx2e1", "4.0*x2",args(sm.getDesignVar("x2")));
Evaluator dg2edx3e1 = expression("dg2edx3e1", "2.0*x3",args(sm.getDesignVar("x3")));
Evaluator dg2edx4e1 = expression("dg2edx4e1"4.0*x41.0",args(sm.getDesignVar("x4")));
List<Evaluator> g2eg1 = list(dg2edx1e1, dg2edx2e1, dg2edx3e1, dg2edx4e1);
sm.setGradientEvaluators("g2", "g2e", "g2eg1", g2eg1);
// response g3:g3e="2.0*x1^2+2.0*x1+x2^2-x2+x3^2-x4-5.0"
// derivativeResponse dg3dx1:dg3edx1 = "4.0*x1+2.0"
// derivativeResponse dg3dx2:dg3edx2 = "2.0*x2-1.0"
// derivativeResponse dg3dx3:dg3edx3 = "2.0*x3"
// derivativeResponse dg3dx4:dg3edx4 = "-1.0"
Evaluator dg3edx1e1 expression("dg3edx1e1""4.0*x1+2.0",args(sm.getDesignVar("x1")));
Evaluator dg3edx2e1 = expression("dg3edx2e1", "2.0*x21.0",args(sm.getDesignVar("x2")));
Evaluator dg3edx3e1 = expression("dg3edx3e1", "2.0*x3",args(sm.getDesignVar("x3")));
Evaluator dg3edx4e1 = expression("dg3edx4e1", "-1.0",args());
List<Evaluator> g3eg1 = list(dg3edx1e1, dg3edx2e1, dg3edx3e1, dg3edx4e1);
sm.setGradientEvaluators("g3", "g3e", "g3eg1", g3eg1);

## Slide 92: Using a SORCER Response Model
Once the model has been defined and configured it can be used.
// you can set the value of the independent variables
rm.setDesignVarValues(set("x1", 2.0), set("x2", 3.0), set("x3", 4.0), set("x4", 200.0));
// print the model
logger.info("\n\nRosen Suzuki response model: " + rm);
// get the values of the responses for the new x values
rm.getRepsonses(); // returns a Table containing the names and values of all Variables. For the Rosen-Suzuki Functions
Data Table [x1,x2,x3,x4,f,g1,g2,g3]
[2.0, 3.0, 4.0, 5.0, 46., 44.0, 71.0, 24.0]
// additional examples of using the api
Var x4 = rm.getDesignVar("x4");
logger.info("\n\nx4 lower bound: " + x4.getLowerBound());
x4 lower bound: -100.0
logger.info("\n\nx4 upper bound: " + x4.getUpperBound());
x4 upper bound: 100.0
logger.info("\n\nx4 value: " + x4.getValue());
x4 value: 5.0
// examine the responseVar f
Var f = rm.getResponseVar("f");
ExpressionEvaluator ee = (ExpressionEvaluator)f.getEvaluator();
logger.info("\n\nexpression:\n" + ee.getName() + "/" + ee.getExpression());
fe/x1^2-5.0*x1+x2^2-5.0*x2+2.0*x3^2-21.0*x3+x4^2+7.0*x4+50.0
logger.info("\n\nresponse:\n" + ee.getName() + "/" + f.getValue());
fe/46.0

## Slide 93: Using a SORCER Response Model
// calculate the sensitivities for a variable
logger.info("----------------- partial derivative f wrt x1 fe|feg1: " + f.getPartialDerivative("x1", "feg1"));
Partial derivative f wrt x1 fe|feg1: -1.0
logger.info("----------------- partial derivative f wrt x3 fe|feg1: " + f.getPartialDerivative("x3", "feg1"));
Partial derivative f wrt x3 fe|feg1: -5.0
// calculate the totalGradient
logger.info("\n\nModel Gradient: " + sm.getTotalGradients());
Model Gradient: [
f:fe[x1, x2, x3, x4]
feg1[-1.0, 1.0, -5.0, 17.0],
[ g1:g1e[x1, x2, x3, x4]
g1eg1[5.0, 5.0, 9.0, 9.0],
g2:g2e[x1, x2, x3, x4]
g2eg1[3.0, 12.0, 8.0, 19.0],
g3:g3e[x1, x2, x3, x4]
g3eg1[10.0, 5.0, 8.0, -1.0]]

## Slide 94: SORCER Parametric Model
SORECER has a parametric Model that allows the performance of a parametric analysis.
ParametricModel paramModel = parametricModel("Parametric Analysis",
designVars("x", designVarCount),
linkedVars("xl1"),
parameterVars("p1"),
responseVars("f"),
responseVars("f",4),
responseVars("g", 3),
parametricTable(input("../data/rosenSuzuki1in.data"),
output("../data/rosenSuzuki1FFout.data", ", ")) );

## Slide 95: SORCER Parametric Model
rosenSuzuki1in.dat
x1 x2 x3 x4
1.1 2.2 3.3 4.4
2.2 4.2 6.6 8.8
4.4 8.8 12.1 16.1
Using the parametric Model
paramModel.evaluate();
paramModel.writeOutputTableToFile();
rosenSuzuki1out.dat
#, p1, x1, x2, x3, x4, xl1, f, f1, f2, f3, f4, g1, g2, g3
50.0, 1, 1.1, 2.2, 3.3, 4.4, 30.800000000000004, 42.190000000000005, 6.050000000000001, 3.3000000000000003, -16.5, 41.14, 26.1, 45.00000000000001, 8.749999999999998
50.0, 2, 2.2, 4.2, 6.6, 8.8, 61.60000000000001, 128.04000000000002, 22.48, 6.4, -32.0, 164.56, 131.27999999999997, 217.56, 57.28
50.0, 3, 4.4, 8.8, 12.1, 16.1, 112.70000000000002, 491.43000000000006, 96.80000000000001, 13.200000000000001, -66.0, 552.03, 486.02, 808.57, 241.47000000000006

## Slide 96: Function of Function Example
The Rosen-Suzuki Function can be expressed
Note: Introduction of Linked Variable and Parameter

## Slide 97: Objective Function, Constraints and Sensitivities
Objective Sensitivities:

## Slide 98: Objective Function, Constraints and Sensitivities
Constraints Sensitivities:

## Slide 99: Function of Function Model Definition
ResponseModel rm = responseModel("Response Analysis",
designVars("x", 4),
linkedVars("xl1"),
parameterVars("p1"),
responseVars("f”),
responseVars("f",4));
ResponseModel sm = responseModel(”Response Analysis",
designVars("x", designVarCount),
linkedVars("xl1"),
realization("xl1", derivative(wrt("x4"))),
parameterVars("p1"),
responseVars("f"),
realization("f", derivative(wrt("f1", "f3", "f4", "x3", "xl1"))),
responseVars("f",4),
realization("f1", derivative(wrt("x1", "x2"))),
realization("f2", derivative(wrt("x1", "x2"))),
realization("f3", derivative(wrt("f2"))),
realization("f4", derivative(wrt("x3", "x4"))),
responseVars("g", 3),
realization("g1", derivative(wrt("f1", "f2", "x2", "x3", "x4"))),
realization("g2", derivative(wrt("x1", "x2", "x3", "x4"))),
realization("g3", derivative(wrt("x1", "x2", "x3", "x4"))));
If the Model will have sensitivities

## Slide 100: Configure the Response Variables in the Model
// configure linked vars
var(model, "xl1", "xl1e", "7.0*x4", args("x4"));
// configure response vars
//f
var(model, "f", "fe", "f1+f3+f4-21.0*x3+xl1+p1", args("f1","f3","f4","x3","xl1","p1"));
//f1
var(model, "f1", "f1e", "x1^2+x2^2", args("x1","x2"));
//f2
var(model, "f2", "f2e", "x1+x2", args("x1","x2"));
//f3
var(model, "f3", "f3e", "-5.0*f2", args("f2"));
//f4
var(model, "f4", "f4e", "2.0*x3^2+x4^2", args("x3","x4"));
//g1
var(model, "g1", "g1e", "f1+f2-2.0*x2+x3^2+x3+x4^2-x4-8.0", args("f1","f2","x2","x3","x4"));
//g2
var(model, "g2", "g2e", "x1^2-x1+2.0*x2^2+x3^2+2.0*x4^2-x4-10.0", args("x1","x2","x3","x4"));
//g3
var(model, "g3", "g3e", "2.0*x1^2+2.0*x1+x2^2-x2+x3^2-x4-5.0", args("x1","x2","x3","x4"));

## Slide 101: Configuration of the Sensitivities
// link variable
Evaluator dfedxl1e = expression("dfedxl1e", "7",args(sm.getDesignVar("x4")));
sm.setGradientEvaluators("xl1", "xl1e", "xl1eg1", list(dfedxl1e));
// response f="f1+f3+f4-21.0*x3+xl1+p1"
// partial derivative df/df1="1.0"
// partial derivative df/df3="1.0"
// partial derivative df/df4="1.0"
// partial derivative df/dx3="-21.0"
// partial derivative df/dxl1="1.0"
Evaluator dfedf1e1 = expression("dfedf1e1", "1.0");
Evaluator dfedf3e1 = expression("dfedf3e1", "1.0");
Evaluator dfedf4e1 = expression("dfedf4e1", "1.0");
Evaluator dfedx3e1 = expression("dfedx3e1", "-21.0");
Evaluator dfedxl1e1 = expression("dfedxl1e1", "1.0");
List<Evaluator> feg1 = list(dfedf1e1, dfedf3e1, dfedf4e1, dfedx3e1, dfedxl1e1);
sm.setGradientEvaluators("f", "fe", "feg1", feg1);
// response f1="x1^2+x2^2"
// partial derivative df1/dx1 ="2.0*x1"
// partial derivative df1/dx2="2.0*x2"
Evaluator df1edx1e1 = expression("df1edx1e1", "2.0*x1",args(sm.getDesignVar("x1")));
Evaluator df1edx2e1 = expression("df1edx2e1", "2.0*x2",args(sm.getDesignVar("x2")));
List<Evaluator> f1eg1 = list(df1edx1e1, df1edx2e1);
sm.setGradientEvaluators("f1", "f1e", "f1eg1", f1eg1);
// response f2="x1+x2"
// partial derivative df2/dx1="1.0"
// partial derivative df2/dx2="1.0"
Evaluator df2edx1e1 = expression("df2edx2e1","1.0");
Evaluator df2edx2e1 = expression("df2edx2e1", "1.0");
List<Evaluator> f2eg1 = list(df2edx1e1, df2edx2e1);
sm.setGradientEvaluators("f2", "f2e", "f2eg1", f2eg1);
/

## Slide 102: Configuration of the Sensitivities
/ response f3="-5.0*f2"
// partial derivative df3/df2="-5.0"
Evaluator df3edf2e1 = expression("df3edf2e1","-5.0");
List<Evaluator> f3eg1 = list(df3edf2e1);
sm.setGradientEvaluators("f3", "f3e", "f3eg1", f3eg1);
// response f4=2.0*x3^2+x4^2
// partial derivative df4/dx3="4.0*x3"
// partial derivative df4/dx4="2.0*x4"
Evaluator df4edx3e1 = expression("df4edx3e1","4.0*x3",args(sm.getDesignVar("x3")));
Evaluator df4edx4e1 = expression("df4edx4e1", "2.0*x4",args(sm.getDesignVar("x4")));
List<Evaluator> f4eg1 = list(df4edx3e1, df4edx4e1);
sm.setGradientEvaluators("f4", "f4e", "f4eg1", f4eg1);
// response g1="f1+f2-2.0*x2+x3^2+x3+x4^2-x4-8.0"
// partial derivative dg1/df1="1.0"
// partial derivative dg1/df2="1.0"
// partial derivative dg1/dx2="-2.0"
// partial derivative dg1/dx3=2.0*x3+1.0"
// partial derivative dg1/dx4=2.0*x4-1.0"
Evaluator dg1edf1e1 = expression("dg1edf1e1", "1.0");
Evaluator dg1edf2e1 = expression("dg1edf2e1", "1.0");
Evaluator dg1edx2e1 = expression("dg1edx2e1", "-2.0");
Evaluator dg1edx3e1 = expression("dg1edx3e1", "2.0*x3+1.0",args(sm.getDesignVar("x3")));
Evaluator dg1edx4e1 = expression("dg1edx4e1", "2.0*x4-1.0",args(sm.getDesignVar("x4")));
List<Evaluator> g1eg1 = list(dg1edf1e1, dg1edf2e1, dg1edx2e1, dg1edx3e1, dg1edx4e1);
sm.setGradientEvaluators("g1", "g1e", "g1eg1", g1eg1);
/

## Slide 103: Configuration of the Sensitivities
/ response g2="x1^2-x1+2.0*x2^2+x3^2+2.0*x4^2-x4-10.0"
// partial derivative dg2dx1 = "2.0*x1-1.0"
// partial derivative dg2dx2 = "4.0*x2"
// partial derivative dg2dx3 = "2.0*x3"
// partial derivative dg2dx4 = "4.0*x4-1.0"
Evaluator dg2edx1e1 = expression("dg2edx1e1", "2.0*x1-1",args(sm.getDesignVar("x1")));
Evaluator dg2edx2e1 = expression("dg2edx2e1", "4.0*x2",args(sm.getDesignVar("x2")));
Evaluator dg2edx3e1 = expression("dg2edx3e1", "2.0*x3",args(sm.getDesignVar("x3")));
Evaluator dg2edx4e1 = expression("dg2edx4e1", "4.0*x4-1.0",args(sm.getDesignVar("x4")));
List<Evaluator> g2eg1 = list(dg2edx1e1, dg2edx2e1, dg2edx3e1, dg2edx4e1);
sm.setGradientEvaluators("g2", "g2e", "g2eg1", g2eg1);
// response g3="2.0*x1^2+2.0*x1+x2^2-x2+x3^2-x4-5.0"
// partial derivative dg3dx1 = "4.0*x1+2.0"
// partial derivative dg3dx2 = "2.0*x2-1.0"
// partial derivative dg3dx3 = "2.0*x3"
// partial derivative dg3dx4 = "-1.0"
Evaluator dg3edx1e1 = expression("dg3edx1e1", "4.0*x1+2.0",args(sm.getDesignVar("x1")));
Evaluator dg3edx2e1 = expression("dg3edx2e1", "2.0*x2-1.0",args(sm.getDesignVar("x2")));
Evaluator dg3edx3e1 = expression("dg3edx3e1", "2.0*x3",args(sm.getDesignVar("x3")));
Evaluator dg3edx4e1 = expression("dg3edx4e1", "-1.0",args());
List<Evaluator> g3eg1 = list(dg3edx1e1, dg3edx2e1, dg3edx3e1, dg3edx4e1);
sm.setGradientEvaluators("g3", "g3e", "g3eg1", g3eg1);

## Slide 104: Using the Function of Function Model
logger.info("*-*-*-*-*-*-*-*-* partial gradients for RozenSuzuki: " + sm.getPartialGradients());
logger.info("*+*+*+*+*+*+*+*+* total gradients for RozenSuzuki: " + sm.getTotalGradients());
logger.info("*+*+*+*+*+*+*+*+* gradient f wrt x1 fe|feg1: " + sm.getGradient("f", "feg1", "x1", "x2"));
Aug 2, 2010 3:27:11 PM sorcer.test.eval.RosenSuzukiFunction1 doFunctionOfFunctionSensitivityAnalysis
[java] INFO: *-*-*-*-*-*-*-*-* partial gradients for RozenSuzuki: [
[java] f:fe[x3, f1, f3, f4, xl1]
[java] feg1[-21.0, 1.0, 1.0, 1.0, 1.0],
[java] f1:f1e[x1, x2]
[java] f1eg1[4.0, 6.0],
[java] f2:f2e[x1, x2]
[java] f2eg1[1.0, 1.0],
[java] f3:f3e[f2]
[java] f3eg1[-5.0],
[java] f4:f4e[x3, x4]
[java] f4eg1[16.0, 10.0],
[java] g1:g1e[x2, x3, x4, f1, f2]
[java] g1eg1[-2.0, 9.0, 9.0, 1.0, 1.0],
[java] g2:g2e[x1, x2, x3, x4]
[java] g2eg1[3.0, 12.0, 8.0, 19.0],
[java] g3:g3e[x1, x2, x3, x4]
[java] g3eg1[10.0, 5.0, 8.0, -1.0],
[java] xl1:xl1e[x4]
[java] xl1eg1[7.0]]

## Slide 105: Using the Function of Function Model
java] Aug 2, 2010 3:27:11 PM sorcer.test.eval.RosenSuzukiFunction1 doFunctionOfFunctionSensitivityAnalysis
[java] INFO: *+*+*+*+*+*+*+*+* total gradients for RozenSuzuki: [
[java] f:fe[x3, f1, f3, f4, xl1]
[java] feg1[-5.0, 1.0, 1.0, 1.0, 1.0],
[java] f1:f1e[x1, x2]
[java] f1eg1[4.0, 6.0],
[java] f2:f2e[x1, x2]
[java] f2eg1[1.0, 1.0],
[java] f3:f3e[f2]
[java] f3eg1[1.0],
[java] f4:f4e[x3, x4]
[java] f4eg1[16.0, 10.0],
[java] g1:g1e[x2, x3, x4, f1, f2]
[java] g1eg1[5.0, 9.0, 9.0, 1.0, 1.0],
[java] g2:g2e[x1, x2, x3, x4]
[java] g2eg1[3.0, 12.0, 8.0, 19.0],
[java] g3:g3e[x1, x2, x3, x4]
[java] g3eg1[10.0, 5.0, 8.0, -1.0],
[java] xl1:xl1e[x4]
[java] xl1eg1[7.0]]
[java] Aug 2, 2010 3:27:11 PM sorcer.test.eval.RosenSuzukiFunction1 doFunctionOfFunctionSensitivityAnalysis
[java] INFO: *+*+*+*+*+*+*+*+* gradient f wrt x1 x2 fe|feg1:
[java] f:fe[x1, x2]
[java] feg1[-1.0, 1.0]
Chain Rule Validation

## Slide 106: Event-driven Exploration: Dispatcher, Model, Optimizer
Model
Dispatcher
Optimizer
Dispatcher#
Notify:ExploreContext
from optimizer
register
update
Dispatcher#
notify:ModelContext
from model
register search
Optimizer#processContext(SearchContext):SearchContext
Modeling#update(Context):void
Modeling#model(Context):Context
Explorer
Explore Context
ExplorerDispatcher#dispatch():void
ExplorerDispatcher#initializeSearchContext(SearchContext):SearchContext
ExplorerDispatcher#updateModelContext(SearchContext):ModelContext
ExplorerDispatcher#updateSearchContext(ModelContext):SearchContext
Explorer#explore(Context):Context
Intra or Inter-processor Exploration
SearchContext
ModelContext

## Slide 107: Var Composition: MBP
Create a model: <model>
Create an Evaluator
Create a Filter
Var var = composition(
<model>, <varName>, <evaluator>, <filter> [<varNameList> | dependents({<varNameList>})])
<varNameList> = list(<varName> {, <varName>} )
Example:
  ResponseModel model;
  Evaluator y1e2 = new GroovyEvaluator("y1e2", "y3 + y4 + y5 + 4*x2^3");
  composition(model, "y1", y1e2, dependents(list("y3", "y4", "y5”), list("x2")));
  Object value = var.getValue(); or value = model.getValue(“y1”);
alternation |
option [ ... ]
repetition { ... }
Notes: MBP – Model Based Programming

## Slide 108: Var Composition: MBP Expressions
Create a model: <model>
ExpressionEvaluator eval = expression(<model>, <varName>, [<evalName>],
<script>,
[<varNameList> | dependents({<varNameList>})], [<evalType>])
Example:
  ResponseModel model; expression(model, “y1”, “y1e1", "xl1 + 2*x2^2 + 3*x3^2 + 5*x4 +4*x2^3”, dependents(list("xl1”, "x2", "x3", "x4")));
  Object value = model.getValue(“y1”);
alternation |
option [ ... ]
repetition { ... }

## Slide 109: Var Composition: MBP & Expression Evaluators
Create a model: <model>
expression([<evalName>],
<script>,
[<varList> | dependents({<varList>})], [<evalType>])
expression([<evalName>], <script>, [<varList> | dependents({<varList>})]) //JEP
groovy([<evalName>], <script>, [<varList> | dependents({<varList>})])
<varList> = varList(<aVar> {, <aVar>} ) | <instanceof VarList>
<aVar> = var(<name>, <value>) | <instanceof Var>
Example:
  ResponseModel model; Evaluator y1e1 = expression("y1e1",
  "xl1 + 2*x2^2 + 3*x3^2 + 5*x4 +4*x2^3”, dependents(model.getVars("xl1”, "x2", "x3", "x4")));
  model.setEvaluator("y1", y1e1);
  Object value = model.getValue(“y1”);
alternation |
option [ ... ]
repetition { ... }

## Slide 110: Var Composition: MBP + VOP API
Create a model
Create an evaluator
Create a filter
Add dependents to the evaluator (model-based var composition)
Assign the evaluator for the variable in the model
Example:
  ResponseModel model; Evaluator y1e2 = expression("y1e2", "y3 + y4 + y5 + 4*x2^3"); Filter y1f2; y1e2.addDependents(model.getVars("y3", "y4", "y5”, "x2")); model.setEvaluation("y1", y1e2, y1f2);
  Object value = model.getValue(“y1”);
alternation |
option [ ... ]
repetition { ... }
Notes: Variable Oriented Programming

## Slide 111: Var Composition: MBP + EOP API
Create a model
Create an exertion
Get an ExertionEvaluator
Add dependents to the evaluator (model-based var composition)
Assign the evaluator for the variable in the model
Example:
  ResponseModel model;
  Exertion exe = new ServiceJob(“service-oriented-colaboration”); … Evaluator y1e = exe.getEvaluator();
  Filter y1f; y1e.addDependents(model.getVars(”y1", ”y2", “x4")); model.setEvaluation("y1", y1e, y1f);
  Object value = model.getValue(“y1”);
alternation |
option [ ... ]
repetition { ... }

## Slide 112: Var Composition: VOP API
Create all related variables
Create an evaluator
Add dependents to the variables (var composition)
Assign the evaluator for the variable
Example:
  Var<Double> y1 = new Var(“y1”, 10.0);
  Var<Double> y3 = … Evaluator y1e2 = new GroovyEvaluator("y1e2", "y3 + y4 + y5 + 4*x2^3"); y1.addDependents(y3, y4, y5, x2)); y1.setEvaluator( y1e2);
  Object value = y1.getValue();
alternation |
option [ ... ]
repetition { ... }

## Slide 113: SORCER Models
SORCER Models support
Analysis – (ResponsModel & ParametricModel)
  multidisciplinary response analysis
  multi-fidelity response analysis
  multi-fidelity response sensitivities
Design Space Exploration (OptimizationModel)
    Optimization
    Multidisciplinary Optimization

## Slide 114: SORCER Variables
SORCER Variable Types (only one)
  Design (default)
  Response
SORCER Variable Kinds (one or more combinations)
  Linked
  Parameter
  Bounded
  Random
  Constraint
  Objective
SORCER Variables are distinguished by four attributes: Type, Kind, ValueType, and MathType
SORCER Variable ValueType (only one)
  Integer
  Long
  Double (Default)
  Float
  String
  Object
  Unknown
  Undefined
SORCER Variable MathType (one or more combinations)
  Continuous (default)
  Discrete
  Discrete_With_Order
  Discrete_with_Math
  Discrete_No_Order
  Problem_Parameter
  ReaL
Example: skinThickness: Type:DESIGN, Kinds:BOUNDED,RANDOM, ValueType:DOUBLE, MathType: REAL, CONTINUOUS

## Slide 115: Variable, Evaluator, Filter (VEF) Design Patterns
Lazy variable evaluation
  getValue vs. evaluate (demand driven calculations)
Evaluator – Decorator pattern
  Evaluator: getValue/evaluate implements EvaluationManagement
  Outer evaluator calls on its inner one
  Evaluator is observable and observer (functional programming)
Observer-Observable
  setChanged
  notify/update
Notes: Function composition is a very powerful way of reusing code and building programs from pieces.
Object composition provides good support for building software from pieces.
Building complete partial results can be a waste of resources, as the next function in the composition chain may need only a few first elements from the partial result variable list, so computing the rest of the list would be a waste of time.
A variable is a generator that, on request (getValue), provides a response-object.

## Slide 116: Basic Variable Structure
y1f3
y1f12
y1
y1e1
dy1dx1e1
dy1dx2e2
dy1dx3e2
dy1dx4e3
Variable
Evaluator
Derivative Evaluators
y1f1
Pipe of Filters

## Slide 117: Advanced Variable Structure
dy1dx1e1 | dy1dx1e4
dy1dx2e2 | dy1dx2e5
dy1dx3e2 | dy1dx3e6
dy1dx3e3 | dy1dx4e7
y1 | y2 | y3
y1e1 | y1e2
dy1dx1e1 | dy1dx1e4
dy1dx2e2 | dy1dx2e5
dy1dx3e2 | dy1dx3e6
dy1dx4e3 | dy1dx4e7
Variables
Evaluators
Gradient Evaluators
Multidisciplinary
Multifidelity
…
…
Drag via N-S Calc.
Drag via Surrogate Calc.

## Slide 118: Model & VEF Example

## Slide 119: Rosen-Suzuki Function Optimization Definition
Minimize
Subject to:

## Slide 120: Objective Function, Constraints and Sensitivities
Objective Sensitivities:
Constraints Sensitivities:

## Slide 121: Constructing a SORCER Response Model
Before constructing the model for the optimization problem just treat the objective and constraints as responses.
Construct a Response Model for these functions.
The steps for constructing a Response Model are
1. Define the Model
2. Configure the Model

## Slide 122: Defining a SORCER Response Model
Define the Model –
  Define the Variables declarativley
    VarOperator , Name of Variable(s) and complementary args for ValueType and MathType
  Define the response & linked realizations for the Variables of Type:
    Name of Evaluator(s) and list of Filter(s) for the Variable(s)
  Define the derivative realizations for the Variable Sensitivities
    Name of var, wrt vars, name of vector of evaluators (default FD Evaluators created)
Example: for the Rosen-Suzuki problem –
Variables: Type:DESIGN, Kind: BOUNDED, MathType:REAL, CONTINUOUS,
ValueType: DOUBLE
Type:RESPONSE, ValueType:DOUBLE

## Slide 123: Defining a SORCER Response Model
ResponseModel rm = ResponseModel(“Rosen-Suzuki Model",
designVars("x", 4), // creates 4 real design varibles x1-x4
responseVars("f"), // creates 1 response variable f
responseVars("g", 3) //creates 3 response variables g1-g3
);
Code for defining the Repsonse Model
The above creates 4 DESIGN variables with names “x1-x4”, 4 RESPONSE variables “f” and “g1-g3”. There are many defaults used when using the minimum specification above.
The following attributes are default for Type DESIGN – the “xi”
ValueType: DOUBLE
MathType: [REAL, CONTINUOUS]
The following attributes are default for Type RESPONSE – the “f”, “gi”
Kind: [ ]
ValueType: DOUBLE
MathType: [REAL, CONTINUOUS]
The following realizations are default for Type RESPONSE – the “f”, “gi” ( default naming convention – variableNamee.)
realization(“f”, evaluation(“fe”),
realization(“g1”, evaluation(“g1e”),
realization(“g2”, evaluation(“g2e”),
realization(“g3”, evaluation(“g3e”)

## Slide 124: Defining a SORCER Response Model
ResponseModel rm = ResponseModel(“Rosen-Suzuki Model",
designVars(var(“x1”, 2.0, -100., 100.), var(“x2”,3.0,-100., 100.),
var(“x3”,4.0, -100, 100.), var(“x4”,5.0, -100, 100.),
responseVars("f"), // creates 1 response variable f
responseVars("g", 3) //creates 3 response variables g1-g3
realization(“f”, evaluation(“fe”),
realization(“g1”, evaluation(“g1e”),
realization(“g2”, evaluation(“g2e”),
realization(“g3”, evaluation(“g3e”)
);
To specify the initial value and bounds on the DESIGN variables and specify the realizations for the RESPONSE variables:
The ResponseModel class has a very rich API

## Slide 125: Defining a SORCER Response Model
Once the Model is defined it must then be configured
For the RESPONSE Variables to have sensitivities one must include them in the realization of the Variable during the definition of the model.
ResponseModel rm = ResponseModel(“Rosen-Suzuki Model",
designVars(var(“x1”, 2.0, -100., 100.), var(“x2”,3.0,-100., 100.),
var(“x3”,4.0, -100, 100.), var(“x4”,5.0, -100, 100.),
responseVars("f"), // creates 1 response variable f
responseVars("g", 3) //creates 3 response variables g1-g3,
realization(“f”, derivate(wrt(“x1”, “x2”, “x3”, “x4”))),
realization(“g1”,derivate(wrt(“x1”,”x2”,”x3”,”x4”))),
realization(“g2”, derivate(wrt(“x1”,”x2”,”x3”,”x4”))),
realization(“g3”, derivate(wrt(“x1”,”x2”,”x3”,”x4”))) )
);

## Slide 126: Configuring a SORCER Response Model
Configuring a Response Model – This requires definition of the EVALUATORS, and FILTERS (if present) for each of the RESPONSE and LINKED variables. For the Rosen-Suzuki case simple expression evaluators are used. No Filters are required.
// configure response variables
// define an evaluator named “fe”, and the variables it depends on. There are several ways to add these dependencies.
Evaluator fe = expression("fe", "x1^2-5.0*x1+x2^2-5.0*x2+2.0*x3^2-21.0*x3+x4^2+7.0*x4+50.0“,
rm.getDesignVars()); // assuming that fe depends on all DesVars in the model.
//Assign this evaluator to the Variable “f” in the Model NOTE: The evaluator name must match the one specified in the realization
model.setResponseEvaluator("f", fe);
// do the same for g1-g3
Evaluator g1e = expression("g1e", "x1^2+x1+x2^2-x2+x3^2+x3+x4^2-x4-8.0");
// another way to add the dependencies
g1e.addDependents(model.getDesignVars("x1", "x2", "x3", "x4"));
model.setResponseEvaluator("g1", g1e);
// another way to add the dependencies
Evaluator g2e = expression("g2e", "x1^2-x1+2.0*x2^2+x3^2+2.0*x4^2-x4-10.0“,
rm.getDesignVars( “x1”, “x2”, “x3”, “x4”));
g2e.addDependents(model.getDesignVars("x1", "x2", "x3", "x4"));
model.setResponseEvaluator("g2", g2e);
Evaluator g3e = expression("g3e", "2.0*x1^2+2.0*x1+x2^2-x2+x3^2-x4-5.0");
model.setResponseEvaluator("g3", g3e);
g3e.addDependents(model.getDesignVars("x1", "x2", "x3", "x4"));

## Slide 127: Configuring a SORCER Response Model
Configuring a Response Model (cont) – If you have evaluators for the sensitivity calculations they need to be configured as well.
// configure the sensitivity model
// response f:fe="x1^2-5.0*x1+x2^2-5.0*x2+2.0*x3^2-21.0*x3+x4^2+7.0*x4+50.0"
// derivativeResponse dfdx1:dfedx1 = "2.0*x1-5.0"
// derivativeResponse dfdx2:dfedx2 = "2.0*x2-5.0"
// derivativeResponse dfdx3:dfedx3 = "4.0*x3-21.0"
// derivativeResponse dfdx4:dfedx4 = "2.0*x4+7.0"
Evaluator dfedx1e1 = expression("dfedx1e1", "2.0*x1-5.0",dependents(sm.getDesignVar("x1")));
Evaluator dfedx2e1 = expression("dfedx2e1", "2.0*x2-5.0",dependents(sm.getDesignVar("x2")));
Evaluator dfedx3e1 = expression("dfedx3e1", "4.0*x3-21.0",dependents(sm.getDesignVar("x3")));
Evaluator dfedx4e1 = expression("dfedx4e1", "2.0*x4+7.0",dependents(sm.getDesignVar("x4")));
List<Evaluator> feg1 = list(dfedx1e1, dfedx2e1, dfedx3e1, dfedx4e1);
sm.setGradientEvaluators("f", "fe", "feg1", feg1);
// response g1:g1e="x1^2+x1+x2^2-x2+x3^2+x3+x4^2-x4-8.0"
// derivativeResponse dg1dx1:dg1edx1 = "2.0*x1+1.0"
// derivativeResponse dg1dx2:dg1edx2 = "2.0*x2-1.0"
// derivativeResponse dg1dx3:dg1edx3 = "2.0*x3+1.0"
// derivativeResponse dg1dx4:dg1edx4 = "2.0*x4-1.0"
Evaluator dg1edx1e1 = expression("dg1edx1e1", "2.0*x1+1",dependents(sm.getDesignVar("x1")));
Evaluator dg1edx2e1 = expression("dg1edx2e1", "2.0*x21.0",dependents(sm.getDesignVar("x2")));
Evaluator dg1edx3e1 = expression("dg1edx3e1""2.0*x3+1.0",dependents(sm.getDesignVar("x3")));
Evaluator dg1edx4e1 = expression("dg1edx4e1", "2.0*x41.0",dependents(sm.getDesignVar("x4")));
List<Evaluator> g1eg1 = list(dg1edx1e1, dg1edx2e1, dg1edx3e1, dg1edx4e1);
sm.setGradientEvaluators("g1", "g1e", "g1eg1", g1eg1);

## Slide 128: Configuring a SORCER Response Model
// response g2:g2e="x1^2-x1+2.0*x2^2+x3^2+2.0*x4^2-x4-10.0"
// derivativeResponse dg2dx1:dg2edx1 = "2.0*x1-1.0"
// derivativeResponse dg2dx2:dg2edx2 = "4.0*x2"
// derivativeResponse dg2dx3:dg2edx3 = "2.0*x3"
// derivativeResponse dg2dx4:dg2edx4 = "4.0*x4-1.0"
Evaluator dg2edx1e1 = expression("dg2edx1e1", "2.0*x11",dependents(sm.getDesignVar("x1")));
Evaluator dg2edx2e1 = expression("dg2edx2e1", "4.0*x2",dependents(sm.getDesignVar("x2")));
Evaluator dg2edx3e1 = expression("dg2edx3e1", "2.0*x3",dependents(sm.getDesignVar("x3")));
Evaluator dg2edx4e1 = expression("dg2edx4e1"4.0*x41.0",dependents(sm.getDesignVar("x4")));
List<Evaluator> g2eg1 = list(dg2edx1e1, dg2edx2e1, dg2edx3e1, dg2edx4e1);
sm.setGradientEvaluators("g2", "g2e", "g2eg1", g2eg1);
// response g3:g3e="2.0*x1^2+2.0*x1+x2^2-x2+x3^2-x4-5.0"
// derivativeResponse dg3dx1:dg3edx1 = "4.0*x1+2.0"
// derivativeResponse dg3dx2:dg3edx2 = "2.0*x2-1.0"
// derivativeResponse dg3dx3:dg3edx3 = "2.0*x3"
// derivativeResponse dg3dx4:dg3edx4 = "-1.0"
Evaluator dg3edx1e1 expression("dg3edx1e1""4.0*x1+2.0",dependents(sm.getDesignVar("x1")));
Evaluator dg3edx2e1 = expression("dg3edx2e1", "2.0*x21.0",dependents(sm.getDesignVar("x2")));
Evaluator dg3edx3e1 = expression("dg3edx3e1", "2.0*x3",dependents(sm.getDesignVar("x3")));
Evaluator dg3edx4e1 = expression("dg3edx4e1", "-1.0",dependents());
List<Evaluator> g3eg1 = list(dg3edx1e1, dg3edx2e1, dg3edx3e1, dg3edx4e1);
sm.setGradientEvaluators("g3", "g3e", "g3eg1", g3eg1);

## Slide 129: Using a SORCER Response Model
Once the model has been defined and configured it can be used.
// you can set the value of the independent variables
rm.setDesignVarValues(set("x1", 2.0), set("x2", 3.0), set("x3", 4.0), set("x4", 200.0));
// print the model
logger.info("\n\nRosen Suzuki response model: " + rm);
// get the values of the responses for the new x values
rm.getRepsonses(); // returns a Table containing the names and values of all Variables. For the Rosen-Suzuki Functions
Data Table [x1,x2,x3,x4,f,g1,g2,g3]
[2.0, 3.0, 4.0, 5.0, 46., 44.0, 71.0, 24.0]
// additional examples of using the api
Var x4 = rm.getDesignVar("x4");
logger.info("\n\nx4 lower bound: " + x4.getLowerBound());
x4 lower bound: -100.0
logger.info("\n\nx4 upper bound: " + x4.getUpperBound());
x4 upper bound: 100.0
logger.info("\n\nx4 value: " + x4.getValue());
x4 value: 5.0
// examine the responseVar f
Var f = rm.getResponseVar("f");
ExpressionEvaluator ee = (ExpressionEvaluator)f.getEvaluator();
logger.info("\n\nexpression:\n" + ee.getName() + "/" + ee.getExpression());
fe/x1^2-5.0*x1+x2^2-5.0*x2+2.0*x3^2-21.0*x3+x4^2+7.0*x4+50.0
logger.info("\n\nresponse:\n" + ee.getName() + "/" + f.getValue());
fe/46.0

## Slide 130: Using a SORCER Response Model
// calculate the sensitivities for a variable
logger.info("----------------- partial derivative f wrt x1 fe|feg1: " + f.getPartialDerivative("x1", "feg1"));
Partial derivative f wrt x1 fe|feg1: -1.0
logger.info("----------------- partial derivative f wrt x3 fe|feg1: " + f.getPartialDerivative("x3", "feg1"));
Partial derivative f wrt x3 fe|feg1: -5.0
// calculate the totalGradient
logger.info("\n\nModel Gradient: " + sm.getTotalGradients());
Model Gradient: [
f:fe[x1, x2, x3, x4]
feg1[-1.0, 1.0, -5.0, 17.0],
[ g1:g1e[x1, x2, x3, x4]
g1eg1[5.0, 5.0, 9.0, 9.0],
g2:g2e[x1, x2, x3, x4]
g2eg1[3.0, 12.0, 8.0, 19.0],
g3:g3e[x1, x2, x3, x4]
g3eg1[10.0, 5.0, 8.0, -1.0]]

## Slide 131: SORCER Parametric Model
SORECER has a parametric Model that allows the performance of a parametric analysis.
ParametricModel paramModel = parametricModel("Parametric Analysis",
designVars("x", designVarCount),
linkedVars("xl1"),
parameterVars("p1"),
responseVars("f"),
responseVars("f",4),
responseVars("g", 3),
parametricTable(input("../data/rosenSuzuki1in.data"),
output("../data/rosenSuzuki1FFout.data", ", ")) );

## Slide 132: SORCER Parametric Model
rosenSuzuki1in.dat
x1 x2 x3 x4
1.1 2.2 3.3 4.4
2.2 4.2 6.6 8.8
4.4 8.8 12.1 16.1
Using the parametric Model
paramModel.evaluate();
paramModel.writeOutputTableToFile();
rosenSuzuki1out.dat
#, p1, x1, x2, x3, x4, xl1, f, f1, f2, f3, f4, g1, g2, g3
50.0, 1, 1.1, 2.2, 3.3, 4.4, 30.800000000000004, 42.190000000000005, 6.050000000000001, 3.3000000000000003, -16.5, 41.14, 26.1, 45.00000000000001, 8.749999999999998
50.0, 2, 2.2, 4.2, 6.6, 8.8, 61.60000000000001, 128.04000000000002, 22.48, 6.4, -32.0, 164.56, 131.27999999999997, 217.56, 57.28
50.0, 3, 4.4, 8.8, 12.1, 16.1, 112.70000000000002, 491.43000000000006, 96.80000000000001, 13.200000000000001, -66.0, 552.03, 486.02, 808.57, 241.47000000000006

## Slide 133: Function of Function Example
The Rosen-Suzuki Function can be expressed
Note: Introduction of Linked Variable and Parameter

## Slide 134: Objective Function, Constraints and Sensitivities
Objective Sensitivities:

## Slide 135: Objective Function, Constraints and Sensitivities
Constraints Sensitivities:

## Slide 136: Function of Function Model Definition
ResponseModel rm = responseModel("Response Analysis",
designVars("x", 4),
linkedVars("xl1"),
parameterVars("p1"),
responseVars("f”),
responseVars("f",4));
ResponseModel sm = responseModel(”Response Analysis",
designVars("x", designVarCount),
linkedVars("xl1"),
realization("xl1", derivative(wrt("x4"))),
parameterVars("p1"),
responseVars("f"),
realization("f", derivative(wrt("f1", "f3", "f4", "x3", "xl1"))),
responseVars("f",4),
realization("f1", derivative(wrt("x1", "x2"))),
realization("f2", derivative(wrt("x1", "x2"))),
realization("f3", derivative(wrt("f2"))),
realization("f4", derivative(wrt("x3", "x4"))),
responseVars("g", 3),
realization("g1", derivative(wrt("f1", "f2", "x2", "x3", "x4"))),
realization("g2", derivative(wrt("x1", "x2", "x3", "x4"))),
realization("g3", derivative(wrt("x1", "x2", "x3", "x4"))));
If the Model will have sensitivities

## Slide 137: Configure the Model
// configure the linkedVariable
Evaluator xl1e = new JepEvaluator("xl1e", "7*x4"); // can use JepEvaluator or expression
xl1e.addDependent(model.getDesignVar("x4"));
model.setLinkedEvaluator("xl1", xl1e);
// configure response vars
Evaluator fe = expression("fe", "f1+f3+f4-21.0*x3+xl1+p1");
model.setResponseEvaluator("f", fe);
fe.addDependents(model.getDesignVars("x3"),model.getResponseVars("f1","f3","f4"));
fe.addDependents(model.getLinkedVar("xl1"));
fe.addDependents(model.getParameterVar("p1"));
Evaluator f1e = expression("f1e", "x1^2+x2^2”, model.getDesignVars("x1","x2"));
model.setResponseEvaluator("f1", f1e);
Evaluator f2e = expression("f2e","x1+x2”, model.getDesignVars("x1","x2"));
model.setResponseEvaluator("f2", f2e);
Evaluator f3e = expression("f3e", "-5.0*f2”, model.getResponseVar("f2"));
model.setResponseEvaluator("f3", f3e);
Evaluator f4e = expression("f4e", "2.0*x3^2+x4^2”, model.getDesignVars("x3","x4”));
model.setResponseEvaluator("f4", f4e);
Evaluator g1e = expression("g1e", "f1+f2-2.0*x2+x3^2+x3+x4^2-x4-8.0");
model.setResponseEvaluator("g1", g1e);
g1e.addDependents(model.getResponseVars("f1", "f2"), model.getDesignVars("x2","x3","x4"));
Evaluator g2e = expression("g2e", "x1^2-x1+2.0*x2^2+x3^2+2.0*x4^2-x4-10.0”, model.getDesignVars());
model.setResponseEvaluator("g2", g2e);
Evaluator g3e = expression("g3e", "2.0*x1^2+2.0*x1+x2^2-x2+x3^2-x4-5.0”, model.getDesignVars());
model.setResponseEvaluator("g3", g3e);

## Slide 138: Configuration of the Sensitivities
// link variable
Evaluator dfedxl1e = expression("dfedxl1e", "7",dependents(sm.getDesignVar("x4")));
sm.setGradientEvaluators("xl1", "xl1e", "xl1eg1", list(dfedxl1e));
// response f="f1+f3+f4-21.0*x3+xl1+p1"
// partial derivative df/df1="1.0"
// partial derivative df/df3="1.0"
// partial derivative df/df4="1.0"
// partial derivative df/dx3="-21.0"
// partial derivative df/dxl1="1.0"
Evaluator dfedf1e1 = expression("dfedf1e1", "1.0");
Evaluator dfedf3e1 = expression("dfedf3e1", "1.0");
Evaluator dfedf4e1 = expression("dfedf4e1", "1.0");
Evaluator dfedx3e1 = expression("dfedx3e1", "-21.0");
Evaluator dfedxl1e1 = expression("dfedxl1e1", "1.0");
List<Evaluator> feg1 = list(dfedf1e1, dfedf3e1, dfedf4e1, dfedx3e1, dfedxl1e1);
sm.setGradientEvaluators("f", "fe", "feg1", feg1);
// response f1="x1^2+x2^2"
// partial derivative df1/dx1 ="2.0*x1"
// partial derivative df1/dx2="2.0*x2"
Evaluator df1edx1e1 = expression("df1edx1e1", "2.0*x1",dependents(sm.getDesignVar("x1")));
Evaluator df1edx2e1 = expression("df1edx2e1", "2.0*x2",dependents(sm.getDesignVar("x2")));
List<Evaluator> f1eg1 = list(df1edx1e1, df1edx2e1);
sm.setGradientEvaluators("f1", "f1e", "f1eg1", f1eg1);
// response f2="x1+x2"
// partial derivative df2/dx1="1.0"
// partial derivative df2/dx2="1.0"
Evaluator df2edx1e1 = expression("df2edx2e1","1.0");
Evaluator df2edx2e1 = expression("df2edx2e1", "1.0");
List<Evaluator> f2eg1 = list(df2edx1e1, df2edx2e1);
sm.setGradientEvaluators("f2", "f2e", "f2eg1", f2eg1);
/

## Slide 139: Configuration of the Sensitivities
/ response f3="-5.0*f2"
// partial derivative df3/df2="-5.0"
Evaluator df3edf2e1 = expression("df3edf2e1","-5.0");
List<Evaluator> f3eg1 = list(df3edf2e1);
sm.setGradientEvaluators("f3", "f3e", "f3eg1", f3eg1);
// response f4=2.0*x3^2+x4^2
// partial derivative df4/dx3="4.0*x3"
// partial derivative df4/dx4="2.0*x4"
Evaluator df4edx3e1 = expression("df4edx3e1","4.0*x3",dependents(sm.getDesignVar("x3")));
Evaluator df4edx4e1 = expression("df4edx4e1", "2.0*x4",dependents(sm.getDesignVar("x4")));
List<Evaluator> f4eg1 = list(df4edx3e1, df4edx4e1);
sm.setGradientEvaluators("f4", "f4e", "f4eg1", f4eg1);
// response g1="f1+f2-2.0*x2+x3^2+x3+x4^2-x4-8.0"
// partial derivative dg1/df1="1.0"
// partial derivative dg1/df2="1.0"
// partial derivative dg1/dx2="-2.0"
// partial derivative dg1/dx3=2.0*x3+1.0"
// partial derivative dg1/dx4=2.0*x4-1.0"
Evaluator dg1edf1e1 = expression("dg1edf1e1", "1.0");
Evaluator dg1edf2e1 = expression("dg1edf2e1", "1.0");
Evaluator dg1edx2e1 = expression("dg1edx2e1", "-2.0");
Evaluator dg1edx3e1 = expression("dg1edx3e1", "2.0*x3+1.0",dependents(sm.getDesignVar("x3")));
Evaluator dg1edx4e1 = expression("dg1edx4e1", "2.0*x4-1.0",dependents(sm.getDesignVar("x4")));
List<Evaluator> g1eg1 = list(dg1edf1e1, dg1edf2e1, dg1edx2e1, dg1edx3e1, dg1edx4e1);
sm.setGradientEvaluators("g1", "g1e", "g1eg1", g1eg1);
/

## Slide 140: Configuration of the Sensitivities
/ response g2="x1^2-x1+2.0*x2^2+x3^2+2.0*x4^2-x4-10.0"
// partial derivative dg2dx1 = "2.0*x1-1.0"
// partial derivative dg2dx2 = "4.0*x2"
// partial derivative dg2dx3 = "2.0*x3"
// partial derivative dg2dx4 = "4.0*x4-1.0"
Evaluator dg2edx1e1 = expression("dg2edx1e1", "2.0*x1-1",dependents(sm.getDesignVar("x1")));
Evaluator dg2edx2e1 = expression("dg2edx2e1", "4.0*x2",dependents(sm.getDesignVar("x2")));
Evaluator dg2edx3e1 = expression("dg2edx3e1", "2.0*x3",dependents(sm.getDesignVar("x3")));
Evaluator dg2edx4e1 = expression("dg2edx4e1", "4.0*x4-1.0",dependents(sm.getDesignVar("x4")));
List<Evaluator> g2eg1 = list(dg2edx1e1, dg2edx2e1, dg2edx3e1, dg2edx4e1);
sm.setGradientEvaluators("g2", "g2e", "g2eg1", g2eg1);
// response g3="2.0*x1^2+2.0*x1+x2^2-x2+x3^2-x4-5.0"
// partial derivative dg3dx1 = "4.0*x1+2.0"
// partial derivative dg3dx2 = "2.0*x2-1.0"
// partial derivative dg3dx3 = "2.0*x3"
// partial derivative dg3dx4 = "-1.0"
Evaluator dg3edx1e1 = expression("dg3edx1e1", "4.0*x1+2.0",dependents(sm.getDesignVar("x1")));
Evaluator dg3edx2e1 = expression("dg3edx2e1", "2.0*x2-1.0",dependents(sm.getDesignVar("x2")));
Evaluator dg3edx3e1 = expression("dg3edx3e1", "2.0*x3",dependents(sm.getDesignVar("x3")));
Evaluator dg3edx4e1 = expression("dg3edx4e1", "-1.0",dependents());
List<Evaluator> g3eg1 = list(dg3edx1e1, dg3edx2e1, dg3edx3e1, dg3edx4e1);
sm.setGradientEvaluators("g3", "g3e", "g3eg1", g3eg1);

## Slide 141
Multi-Fidelity for the Responses and Sensitivities

## Slide 142: Objective Function Multi-Fidelity

## Slide 143: Constraint Functions Multi-Fidelity
Two Evaluators for G1
Single Evaluators for G2 & G3

## Slide 144: Objective Sensitivities with Multi-Fidelity

## Slide 145: Objective Sensitivities with Multi-Fidelity
Multi-Fidelity Sensitivities for the Multi-Fidelity Objective

## Slide 146: Multi-Fidelity Constraints & Multi-Fidelity Sensitivities

## Slide 147: Constraint Sensitivities

## Slide 148: Model Definition with Multi-Fidelity Responses and Sensitivities
ResponseModel sm = responseModel("Sensitivity Analysis",
designVars("x", 4),
linkedVars("xl1"),
parameterVars("p1"),
responseVars("f"),
realization("f", evaluation("fe1"), evaluation("fe2"),
derivative("fe1", wrt("x1", "x2", "x3", "x4"), gradient("fe1g1"), gradient("fe1g2") ),
derivative("fe2", wrt("f1", "f3", "f4", "x3", "xl1”), gradient("fe2g1"), gradient("fe2g2") )),
responseVars("f",4),
realization("f1", derivative(wrt("x1", "x2")) ),
realization("f2", derivative(wrt("x1", "x2")) ),
realization("f3", derivative(wrt("f2"))),
realization("f4", evaluation("f4e"),
derivative("f4e", wrt("x3", "x4"), gradient("f4eg1"), gradient("f4eg2")) ),
responseVars("g", 3),
realization("g1", evaluation("g1e1"), evaluation("g1e2"),
derivative("g1e1", wrt("x1", "x2", "x3", "x4"), gradient("g1e1g1"), gradient("g1e1g2") ),
derivative("g1e2", wrt("f1", "f2", "x2", "x3", "x4"), gradient("g1e2g1"), gradient("g1e2g2") ) ) ,
realization("g2", derivative(wrt("x1", "x2", "x3", "x4"))),
realization("g3", derivative(wrt("x1", "x2", "x3", "x4"))));
NOTE: With Multi-Fidelity the realizations MUST be Defined in the Model

## Slide 149: Model Configuration
// f:fe1
// design vars: x1, x2, x3, x4
// response vars: f
// response f:fe1="x1^2-5.0*x1+x2^2-5.0*x2+2.0*x3^2-21.0*x3+x4^2+7.0*x4+50.0"
//dfdxi:dfe1dxie1
// partial derivative dfe1dx1e1 = "2.0*x1-5.0"
// partial derivative dfe1dx2e1 = "2.0*x2-5.0"
// partial derivative dfe1dx3e1 = "4.0*x3-21.0"
// partial derivative dfe1dx4e1 = "2.0*x4+7.0"
Evaluator dfe1dx1e1 = expression("dfe1dx1e1", "2.0*x1-5.0",dependents(sm.getDesignVar("x1")));
Evaluator dfe1dx2e1 = expression("dfe1dx2e1", "2.0*x2-5.0",dependents(sm.getDesignVar("x2")));
Evaluator dfe1dx3e1 = expression("dfe1dx3e1", "4.0*x3-21.0",dependents(sm.getDesignVar("x3")));
Evaluator dfe1dx4e1 = expression("dfe1dx4e1", "2.0*x4+7.0",dependents(sm.getDesignVar("x4")));
List<Evaluator> fe1g1 = list(dfe1dx1e1, dfe1dx2e1, dfe1dx3e1, dfe1dx4e1);
sm.setGradientEvaluators("f", "fe1", "fe1g1", fe1g1);
//dfdxi:dfe1dxie2
// partial derivative dfe1dx1e2 = (fe1(x1+deltax1) -fe1(x1))/deltax1
// partial derivative dfe1dx2e2 = (fe1(x2+deltax2) -fe1(x1))/deltax2
// partial derivative dfe1dx3e2 = (fe1(x3+deltax3) -fe1(x1))/deltax3
// partial derivative dfe1dx4e2 = (fe1(x4+deltax4) -fe1(x1))/deltax4
Evaluator dfe1dx1e2 = new FiniteDifferenceEvaluator("dfe1dx1e2", sm.getResponseVar("f").getEvaluator("fe1"),0.1, "x1");
Evaluator dfe1dx2e2 = new FiniteDifferenceEvaluator("dfe1dx2e2", sm.getResponseVar("f").getEvaluator("fe1"),0.1, "x2");
Evaluator dfe1dx3e2 = new FiniteDifferenceEvaluator("dfe1dx3e2", sm.getResponseVar("f").getEvaluator("fe1"),0.1, "x3");
Evaluator dfe1dx4e2 = new FiniteDifferenceEvaluator("dfe1dx4e2", sm.getResponseVar("f").getEvaluator("fe1"),0.1, "x4");
List<Evaluator> fe1g2 = list(dfe1dx1e2, dfe1dx2e2, dfe1dx3e2, dfe1dx4e2);
sm.setGradientEvaluators("f", "fe1", "fe1g2", fe1g2);
// link variable
Evaluator dfe1dxl1e = expression("dfe1dxl1e", "7",dependents(sm.getDesignVar("x4")));
sm.setGradientEvaluators("xl1", "xl1e", "xl1eg", list(dfe1dxl1e));

## Slide 150: Fe2 with with Multi-Fidelity Sensitivities
// f:fe2
// design vars: x1, x2, x3, x4
// linked vars: xl1="7.0*x4"
// parameters: p1=50.
// response vars: f, f1, f2, f3, f4,
// response f:fe2="f1+f3+f4-21.0*x3+xl1+p1"
// dfdxi:dfe2dxie1
// partial derivative dfe2df1e1="1.0"
// partial derivative dfe2df3e1="1.0"
// partial derivative dfe2df4e1="1.0"
// partial derivative dfe2dx3e1="-21.0"
// partial derivative dfe2dxl1e1="1.0"
Evaluator dfe2df1e1 = expression("dfe2df1e1", "1.0");
Evaluator dfe2df3e1 = expression("dfe2df3e1", "1.0");
Evaluator dfe2df4e1 = expression("dfe2df4e1", "1.0");
Evaluator dfe2dx3e1 = expression("dfe2dx3e1", "-21.0");
Evaluator dfe2dxl1e1 = expression("dfe2dxl1e1", "1.0");
Evaluator dfe2dp1e1 = expression("dfe2dp1e1", "0.0");
List<Evaluator> fe2g1 = list(dfe2df1e1, dfe2df3e1, dfe2df4e1, dfe2dx3e1, dfe2dxl1e1, dfe2dp1e1);
sm.setGradientEvaluators("f", "fe2", "fe2g1", fe2g1);
// dfdxi:dfe2dxie2
// partial derivative dfe2df1e2 = (fe2(f1+deltaf1) -fe2(f1))/deltaf1
// partial derivative dfe2df3e2 = (fe2(f3+deltaf3) -fe2(f3))/deltaf3
// partial derivative dfe2df4e2 = (fe2(f4+deltaf4) -fe2(f4))/deltaf4
// partial derivative dfe2dx3e2 = (fe2(x3+deltax3) -fe2(x3))/deltax3
// partial derivative dfe2dxl1e2 = (fe2(xl1+deltaxl1) -fe2(x1l))/deltaxl1
Evaluator dfe2df1e2 = new FiniteDifferenceEvaluator("dfe2df1e2", sm.getResponseVar("f").getEvaluator("fe2"), 0.1, "f1");
Evaluator dfe2df3e2 = new FiniteDifferenceEvaluator("dfe2df3e2", sm.getResponseVar("f").getEvaluator("fe2"), 0.1, "f3");
Evaluator dfe2df4e2 = new FiniteDifferenceEvaluator("dfe2df4e2", sm.getResponseVar("f").getEvaluator("fe2"), 0.1, "f4");
Evaluator dfe2dx3e2 = new FiniteDifferenceEvaluator("dfe2dx3e2", sm.getResponseVar("f").getEvaluator("fe2"), 0.1, "x3");
Evaluator dfe2dxl1e2 = new FiniteDifferenceEvaluator("dfe2dxl1e2", sm.getResponseVar("f").getEvaluator("fe2"), 0.1, "xl1");
Evaluator dfe2dp1e2 = expression("dfe2dp1e2", "0.0");
List<Evaluator> fe2g2 = list(dfe2df1e2, dfe2df3e2, dfe2df4e2, dfe2dx3e2, dfe2dxl1e2,dfe2dp1e2 );
sm.setGradientEvaluators("f", "fe2", "fe2g2", fe2g2);

## Slide 151
// response f1="x1^2+x2^2"
// partial derivative df1/dx1 ="2.0*x1"
// partial derivative df1/dx2="2.0*x2"
Evaluator df1edx1e1 = expression("df1edx1e1", "2.0*x1",dependents(sm.getDesignVar("x1")));
Evaluator df1edx2e1 = expression("df1edx2e1", "2.0*x2",dependents(sm.getDesignVar("x2")));
List<Evaluator> f1eg1 = list(df1edx1e1, df1edx2e1);
sm.setGradientEvaluators("f1", "f1e", "f1eg1", f1eg1);
// response f2="x1+x2"
// partial derivative df2/dx1="1.0"
// partial derivative df2/dx2="1.0"
Evaluator df2edx1e1 = expression("df2edx2e1","1.0");
Evaluator df2edx2e1 = expression("df2edx2e1", "1.0");
List<Evaluator> f2eg1 = list(df2edx1e1, df2edx2e1);
sm.setGradientEvaluators("f2", "f2e", "f2eg1", f2eg1);
// response f3="-5.0*f2"
// partial derivative df3/df2="-5.0"
Evaluator df3edf2e1 = expression("df3edf2e1","-5.0");
List<Evaluator> f3eg1 = list(df3edf2e1);
sm.setGradientEvaluators("f3", "f3e", "f3eg1", f3eg1);
// response f4:f4e=2.0*x3^2+x4^2
// df4dxie1
// partial derivative df4/dx3:df4edx1e1="4.0*x3"
// partial derivative df4/dx4:df4edx4e1="2.0*x4"
Evaluator df4edx3e1 = expression("df4edx3e1","4.0*x3",dependents(sm.getDesignVar("x3")));
Evaluator df4edx4e1 = expression("df4edx4e1", "2.0*x4",dependents(sm.getDesignVar("x4")));
List<Evaluator> f4eg1 = list(df4edx3e1, df4edx4e1);
sm.setGradientEvaluators("f4", "f4e", "f4eg1", f4eg1);
// df4dxie2
// partial derivative df4/dx3:df4edx3e2=(f4e(x3+deltax3) -f4e(x3))/deltax3
// partial derivative df4/dx4:df4edx4e2=(f4e(x4+deltax4) -f4e(x4))/deltax4
Evaluator df4edx3e2 = new FiniteDifferenceEvaluator("df4edx3e2", sm.getResponseVar("f4").getEvaluator("f4e"), 0.1, "x2");
Evaluator df4edx4e2 = new FiniteDifferenceEvaluator("df4edx4e2", sm.getResponseVar("f4").getEvaluator("f4e"), 0.1, "x4");
List<Evaluator> f4eg2 = list(df4edx3e2, df4edx4e2);
sm.setGradientEvaluators("f4", "f4e", "f4eg2", f4eg2);

## Slide 152
//g1: g1e1
// response g1:g1e1="x1^2+x1+x2^2-x2+x3^2+x3+x4^2-x4-8.0"
// dg1e1dxie1
// derivativeResponse dg1dx1:dg1e1dx1 = "2.0*x1+1.0"
// derivativeResponse dg1dx2:dg1e1dx2 = "2.0*x2-1.0"
// derivativeResponse dg1dx3:dg1e1dx3 = "2.0*x3+1.0"
// derivativeResponse dg1dx4:dg1e1dx4 = "2.0*x4-1.0"
Evaluator dg1e1dx1e1 = expression("dg1e1dx1e1", "2.0*x1+1",dependents(sm.getDesignVar("x1")));
Evaluator dg1e1dx2e1 = expression("dg1e1dx2e1", "2.0*x2-1.0",dependents(sm.getDesignVar("x2")));
Evaluator dg1e1dx3e1 = expression("dg1e1dx3e1", "2.0*x3+1.0",dependents(sm.getDesignVar("x3")));
Evaluator dg1e1dx4e1 = expression("dg1e1dx4e1", "2.0*x4-1.0",dependents(sm.getDesignVar("x4")));
List<Evaluator> g1e1g1 = list(dg1e1dx1e1, dg1e1dx2e1, dg1e1dx3e1, dg1e1dx4e1);
sm.setGradientEvaluators("g1", "g1e1", "g1e1g1", g1e1g1);
// dg1e1dxie2
Evaluator dg1e1dx1e2 = new FiniteDifferenceEvaluator("dg1e1dx1e2", sm.getResponseVar("g1").getEvaluator("g1e1"), 0.1, "x1");
Evaluator dg1e1dx2e2 = new FiniteDifferenceEvaluator("dg1e1dx2e2", sm.getResponseVar("g1").getEvaluator("g1e1"), 0.1, "x2");
Evaluator dg1e1dx3e2 = new FiniteDifferenceEvaluator("dg1e1dx3e2", sm.getResponseVar("g1").getEvaluator("g1e1"), 0.1, "x3");
Evaluator dg1e1dx4e2 = new FiniteDifferenceEvaluator("dg1e1dx4e2", sm.getResponseVar("g1").getEvaluator("g1e1"), 0.1, "x4");
List<Evaluator> g1e1g2 = list(dg1e1dx1e2, dg1e1dx2e2, dg1e1dx3e2, dg1e1dx4e2);
sm.setGradientEvaluators("g1", "g1e1", "g1e1g2", g1e1g2);

## Slide 153
//g1: g1e2
// response g1:g1e2="f1+f2-2.0*x2+x3^2+x3+x4^2-x4-8.0"
// partial derivative dg1/df1="1.0"
// partial derivative dg1/df2="1.0"
// partial derivative dg1/dx2="-2.0"
// partial derivative dg1/dx3=2.0*x3+1.0"
// partial derivative dg1/dx4=2.0*x4-1.0"
// dg1e2dxie1
Evaluator dg1e2df1e1 = expression("dg1e2df1e1", "1.0");
Evaluator dg1e2df2e1 = expression("dg1e2df2e1", "1.0");
Evaluator dg1e2dx2e1 = expression("dg1e2dx2e1", "-2.0");
Evaluator dg1e2dx3e1 = expression("dg1e2dx3e1", "2.0*x3+1.0",dependents(sm.getDesignVar("x3")));
Evaluator dg1e2dx4e1 = expression("dg1e2dx4e1", "2.0*x4-1.0",dependents(sm.getDesignVar("x4")));
List<Evaluator> g1e2g1 = list(dg1e2df1e1, dg1e2df2e1, dg1e2dx2e1, dg1e2dx3e1, dg1e2dx4e1);
sm.setGradientEvaluators("g1", "g1e2", "g1e2g1", g1e2g1);
// dg1e2dxie2
Evaluator dg1e2df1e2 = new FiniteDifferenceEvaluator("dg1e2df1e2", sm.getResponseVar("g1").getEvaluator("g1e2"), 0.1, "f1");
Evaluator dg1e2df2e2 = new FiniteDifferenceEvaluator("dg1e2df2e2", sm.getResponseVar("g1").getEvaluator("g1e2"), 0.1, "f2");
Evaluator dg1e2dx2e2 = new FiniteDifferenceEvaluator("dg1e2dx2e2", sm.getResponseVar("g1").getEvaluator("g1e2"), 0.1, "x2");
Evaluator dg1e2dx3e2 = new FiniteDifferenceEvaluator("dg1e2dx3e2", sm.getResponseVar("g1").getEvaluator("g1e2"), 0.1, "x3");
Evaluator dg1e2dx4e2 = new FiniteDifferenceEvaluator("dg1e2dx4e2", sm.getResponseVar("g1").getEvaluator("g1e2"), 0.1, "x4");
List<Evaluator> g1e2g2 = list(dg1e2df1e2, dg1e2df2e2, dg1e2dx2e2, dg1e2dx3e2, dg1e2dx4e2);
sm.setGradientEvaluators("g1", "g1e2", "g1e2g2", g1e2g2);

## Slide 154
// response g2="x1^2-x1+2.0*x2^2+x3^2+2.0*x4^2-x4-10.0"
// partial derivative dg2dx1 = "2.0*x1-1.0"
// partial derivative dg2dx2 = "4.0*x2"
// partial derivative dg2dx3 = "2.0*x3"
// partial derivative dg2dx4 = "4.0*x4-1.0"
Evaluator dg2edx1e1 = expression("dg2edx1e1", "2.0*x1-1",dependents(sm.getDesignVar("x1")));
Evaluator dg2edx2e1 = expression("dg2edx2e1", "4.0*x2",dependents(sm.getDesignVar("x2")));
Evaluator dg2edx3e1 = expression("dg2edx3e1", "2.0*x3",dependents(sm.getDesignVar("x3")));
Evaluator dg2edx4e1 = expression("dg2edx4e1", "4.0*x4-1.0",dependents(sm.getDesignVar("x4")));
List<Evaluator> g2eg1 = list(dg2edx1e1, dg2edx2e1, dg2edx3e1, dg2edx4e1);
sm.setGradientEvaluators("g2", "g2e", "g2eg1", g2eg1);
// response g3="2.0*x1^2+2.0*x1+x2^2-x2+x3^2-x4-5.0"
// partial derivative dg3dx1 = "4.0*x1+2.0"
// partial derivative dg3dx2 = "2.0*x2-1.0"
// partial derivative dg3dx3 = "2.0*x3"
// partial derivative dg3dx4 = "-1.0"
Evaluator dg3edx1e1 = expression("dg3edx1e1", "4.0*x1+2.0",dependents(sm.getDesignVar("x1")));
Evaluator dg3edx2e1 = expression("dg3edx2e1", "2.0*x2-1.0",dependents(sm.getDesignVar("x2")));
Evaluator dg3edx3e1 = expression("dg3edx3e1", "2.0*x3",dependents(sm.getDesignVar("x3")));
Evaluator dg3edx4e1 = expression("dg3edx4e1", "-1.0",dependents());
List<Evaluator> g3eg1 = list(dg3edx1e1, dg3edx2e1, dg3edx3e1, dg3edx4e1);
sm.setGradientEvaluators("g3", "g3e", "g3eg1", g3eg1);

## Slide 155: Using the Multi-Fidelity Model
sm.setDesignVarValues(set("x1", 2.0), set("x2", 3.0), set("x3", 4.0), set("x4", 5.0));
sm.setParameterVarValues(set("p1", 50.0));
//logger.info("\n\ndoSensitivityAnalysis out: " + sm.getSensitivities());
Var f = sm.getResponseVar("f");
logger.info("\n fe1 fe1g2 ******************************************************************:\n "+sm.getPartialGradients() );
// Check the partial derivative calculations
//f
// fe1/g1 partials
f.selectEvaluator("fe1");
logger.info("\n current f function value:\n" + f.getValue());
//logger.info("\n fe1 fe1g1 ******************************************************************:\n" );
//logger.info("-- partial derivative f wrt x1 with evaluator fe1 gradient fe1g1 fe1|fe1g1: " + f.getPartialDerivative("x1", "fe1g1"));
//logger.info("-- partial derivative f wrt x2 with evaluator fe1 gradient fe1g1 fe1|fe1g1: " + f.getPartialDerivative("x2", "fe1g1"));
//logger.info("-- partial derivative f wrt x3 with evaluator fe1 gradient fe1g1 fe1|fe1g1: " + f.getPartialDerivative("x3", "fe1g1"));
//logger.info("-- partial derivative f wrt x4 with evaluator fe1 gradient fe1g1 fe1|fe1g1: " + f.getPartialDerivative("x4", "fe1g1"));
//logger.info("-- partial gradient f wrt xi with evaluator fe1 gradient fe1g1 fe1|fe1g1: " + f.getPartialGradient("fe1g1"));
// fe1/g2 partials
//logger.info("-- partial derivative f wrt x1 with evaluator fe1 gradient fe1g2 fe1|fe1g2: " + f.getPartialDerivative("x1", "fe1g2"));
//logger.info("-- partial derivative f wrt x2 with evaluator fe1 gradient fe1g2 fe1|fe1g2: " + f.getPartialDerivative("x2", "fe1g2"));
//logger.info("-- partial derivative f wrt x3 with evaluator fe1 gradient fe1g2 fe1|fe1g2: " + f.getPartialDerivative("x3", "fe1g2"));
//logger.info("-- partial derivative f wrt x4 with evaluator fe1 gradient fe1g2 fe1|fe1g2: " + f.getPartialDerivative("x4", "fe1g2"));
//logger.info("-- partial gradient f wrt xi with evaluator fe1 gradient fe1g2 fe1|fe1g2: " + f.getPartialGradient("fe1g2"));
// fe2/g1 partials
f.selectEvaluator("fe2");
logger.info("\n fe2 fe2g1 ******************************************************************:\n" );
logger.info("-- partial derivative f wrt f1 with evaluator fe2 gradient fe2g1 fe1|feg1: " + f.getPartialDerivative("f1", "fe2g1"));
logger.info("-- partial derivative f wrt f3 with evaluator fe2 gradient fe2g1 fe1|feg1: " + f.getPartialDerivative("f3", "fe2g1"));
logger.info("-- partial derivative f wrt f4 with evaluator fe2 gradient fe2g1 fe1|feg1: " + f.getPartialDerivative("f4", "fe2g1"));
logger.info("-- partial derivative f wrt x3 with evaluator fe2 gradient fe2g1 fe1|feg1: " + f.getPartialDerivative("x3", "fe2g1"));
logger.info("-- partial derivative f wrt xl1 with evaluator fe2 gradient fe2g1 fe1|feg1: " + f.getPartialDerivative("xl1", "fe2g1"));

## Slide 156: Optimization Model Definition
OptimizationModel om = optimizationModel("DesignExploration Model",
designVars("x", 4),
responseVars("f"),
responseVars("g",3),
objectiveVars(var("fo", "f", Target.min )),
constraintVars(var("g1c", "g1", Relation.lt, 0.0),
var("g2c", "g2", Relation.lt, 0.0),
var("g3c","g3",Relation.lt, 0.0)));

## Slide 157: MSTC SORCER Applications to Date
Hi-Fidelity Aeroelastic Analysis
  Euler (AVUS), FEM (MSCNASTRAN), MDICE
Hi-Fidelity Induced Drag minimization
  Euler (AVUS), Optimization (CONMIN, MATLAB)
2-D large amplitude airfoil motion trajectory Optimization
  Unsteady Vortex Lattice Method (in-house UVLM), Opti (DOT)
Shape and sizing aeroelastic optimization
  Euler (AVUS), FEM (MSCNASTRAN), MDICE, Opti (DOT) FD sensitivities
Demonstrated tight integration with C, C++, and FORTRAN using JNA (can make direct calls to any shared object)
Network configuration
  Linux workstations
  Linux cluster(2), Mac cluster(1)
  SGI Irix
  Windows
  Mac Desktop
  Mac laptop

## Slide 158: Shape and Sizing Aeroelastic Optimization
Minimize
Objective Function
Subject to
Inequality
Constraints
Side
Constraints
Ernest Thompson – AFRL/RBSD
- Structural sizes, and planform sweep
Notes: Challenges

## Slide 159: Min weight shape & sizing opti
Mach
q_rev
Ernest Thompson – AFRL/RBSD
- Euler Static Aeroelastic Calculations

## Slide 160: Sorcer network configuration for min weight (shape and sizing)
Gladius
Client
Coalescence
NMEDA
Avus
Avus
Avus
Xserv2
Whittle
Gothmog
RBSDZ0010143
Ernest Thompson – AFRL/RBSD

## Slide 161: Concluding Remarks
MSTC is responsible for executing large scale system level MDA/MDO in a heterogenous computing environment
SORCER exposes Sun’s Jini connection Technology to create a Model Oriented Programming (MOP) and computing environment for large scale MDA/MDO
SORCER Functionality
  Create providers and expose them as jini services.
  Exertion Oriented Programming – Ability to orchastrate Services
  Models for analysis, sensitvitities, and design
  VEF – Functional demand driven computations
  Space Computing

## Slide 162
Backup Slides

## Slide 163: Motivation
Long duration on station
Large changes of over the mission

## Slide 164: A Solution
Utilize conformal control surfaces to enhance laminar flow, minimize the Drag
FlexSys Inc.
Adaptive Compliant Wing

## Slide 165: How to Determine the Compliant Surface Settings?
Approach 1. Indirect – Given a load distribution that is known to minimize drag, determine the control surface settings to obtain the desired load distribution.
Approach 2. Direct - Minimization of drag ( induced drag currently) using the conformal control surface settings.

## Slide 167: Trefftz-Plane Induced Drag With Euler Aerodynamics
(Kutta-Joukowski theorem)

## Slide 168: Optimization Problem
Computation of Lpus requires Euler Solution at Transonic Mach #s

## Slide 169
Evaluators for Induced Drag and Sensitivities
Standard One Point Approximation (SOA) – Perform Euler solutions
Exact – Perform Euler solution for
By FD Euler Solutions
Kriging – Perform Euler solutions (hundreds) for Kriging Model
Modified One Point Approximation (MOA) – Perform Euler solution

## Slide 170: Induced Drag Optimization Model
OptimizationModel omodel = optimizationModel("Induced Drag",
designVars(vars(loop("i",1,20),"beta$i$", 0.0, -10.0, 10.0)),
linkedVars(names(loop("i",21,40),"betal$i$")),
designVars(var("alpha", 5.0, -5.0, 10.0)),
designVars("mach", "gamma", "pstatic"),
responseVars(var("DI",
realization(
evaluation("DIExacte",
differentiation(wrt(names(loop("i",1,20),"beta$i$"), "alpha","q"), gradient("DIExacteg1"))),
evaluation("DISOAe",
differentiation(wrt(names(loop("i",1,20),"beta$i$"), "alpha","q"), gradient("DISOAeg1"))),
evaluation("DIMOAe",
differentiation(wrt(names(loop("i",1,20),"beta$i$"), "alpha","q"), gradient("DIMOAeg1"))),
evaluation("DIKrige",
differentiation(wrt(names(loop("i",1,20),"beta$i$"), "alpha","q"), gradient("DIKrigeg1")))))),
responseVars(var("LT",
realization(
evaluation("LTExacte",
differentiation(wrt(names(loop("i",1,20),"beta$i$"), "alpha","q"), gradient("LTExacteg1"))),
evaluation("LTSOAe",
differentiation(wrt(names(loop("i",1,20),"beta$i$"), "alpha","q"), gradient("LTSOAeg1"))),
evaluation("LTMOAe",
differentiation(wrt(names(loop("i",1,20),"beta$i$"), "alpha","q"), gradient("LTMOAeg1")))))),
responseVars(loop("i",1,20),"Lpus$i$",
realization(
evaluation("Lpus$i$Exacte",
differentiation(wrt(names(loop("k",1,20),"beta$k$"), "alpha"), gradient("Lpus$i$Exacteg1"))),
evaluation("Lpus$i$SOAe",
differentiation(wrt(names(loop("k",1,20),"beta$k$"), "alpha"), gradient("Lpus$i$SOAeg1"))))),
responseVars(var("q",
realization(evaluation("qExact", differentiation(wrt("mach","gamma","pstatic"), gradient("qExactg1")))))),
objectiveVars(var("DIo", "DI", Target.min )),
constraintVars(var("LTc", "LT", Relation.eq, 1000.0))
);

## Slide 171: Service Oriented Computing EnvirRonment (SORCER)
SORCER Enables Seamless Access to All Methods, Models, Data, and Computing Resources
AVUS Provider
Euler Drag
Calculations
Coalescence – Linux Beau Wolf Cluster
Numerical Analysis Provider
Gradient Calculations
Nelson – SGI Irix 6.5
DNA – Linux Desk Top
Optimization Provider
Approximations
CONMIN Optimization
Client
Sobolewski, M., Kolonay, R “Federated Grid Computing with Interactive Service-oriented Programming,” International Journal of Concurrent Engineering: Research & Applications, Vol. 14, No 1 2006 pp. 55-66

## Slide 172: Example Case
Goland Wing Planform with a NACA 0006 Airfoil
(Euler Calculations- AVUS (1.5 million cells)
20 Control surfaces @ 20% c
20 ft semi span

## Slide 173: Modified First Order Taylor Series Approximation
 | Value | % Diff
Exact Function | 1.18388E-03 | 0.0%
Tradition First Order Taylor Series Expansion | -4.380E-04 | -137%
Modified First Order Taylor Series Expansion | 1.18708E-03 | 0.27%
Comparison of Traditional and Modified First Order Taylor Series Expansion

## Slide 174: Goland Wing M=0.85, Alpha=5.0
Square Error Objective
versus
Outer Loop Iteration
Iteration #
Square Error
*Lift constraint satisfied to within 0.3%
Spanwise strip
CL per Span
CL per Span Versus Spanwise Strip

## Slide 175: Goland Wing M=0.85, Alpha=5.0
Upper Surface
Upper Surface
Lower Surface
Lower Surface
Cp Initial
Cp Final
0.876
-0.662
degrees

## Slide 176: Concluding Remarks
Have a process implemented that enables minimum induced drag optimization with an Euler solver.
Transpiration Boundary Conditions working very well to simulate control surface deflections.
Modified First Order Taylor Series Expansion extremely accurate
Next Steps
  Static Aeroelastic effects included
  Develop appropriate induced Drag calculation
  Investigate assumption of
  Being linear about nonlinear static equilibrium

## Slide 177
Task – Avus Task
Context - AvusContext
"AVUS/BCFILE",URL_to_AVUS_BC_FILE
"AVUS/JOBFILE", URL_to_AVUS_JOB_FILE
"AVUS/RESTARTFILE", URL_to_AVUS_JOB_RESTART_FILE
"AVUS/GRIDFILE", URL_to_AVUS_GRID_FILE
"AVUS/TAPFILE",URL_to_AVUS_TAP_FILE
"AVUS/TRIPFILE", URL_to_AVUS_TRIP_FILE
"AVUS/AVUSOUTPUT",AVUS_OUTPUT_OBJECT
MethodSignature – AvusMethod ServiceSignature(engineering.provider.avus.AvusRemoteInterface.class)

## Slide 178: Optimization Model
Note: Multi-fidelity for responses
ResponseModel sm = responseModel(”Induced Drag",
designVars(“cs", 20, 0.0, -10.0, 10.0),
designVars(“alpha”, 1.0, -5.0, 5.0),
linkedVars(”beta”,20,21),
designVars(“v0”),
designVars(“rho”),
responseVars(“DI"),
responseVars(“Lpus”,20),
responseVars(“qdp”),
realization(“DI", evaluation(“DIeExact"), evaluation(”DIeSOA”), evaluation(“DIeMOA”), evaluatioin(“DIeKrig”),
derivative("DIeExact", wrt(”betai", “alpha”), gradient(“DIExactg1”)),
derivative("DIeSOA", wrt(”betai", “alpha”), gradient(“DIExactg1”)),
derivative("DIeMOAt", wrt(”betai", “alpha”), gradient(“DIExactg1”)),
derivative("DIeKrig", wrt(”betai", “alpha”), gradient(“DIExactg1”)),
responseVars(“Ltot”),
realization(”Ltot", derivative(wrt(“betai”,”alpha”)) ),
realization(”Lpus1", evaluation(“Lpus1Exact”), evaluation(“Lpus1SOA”),
derivative(wrt(”betai", ”alpha")) ),
…
realization(”Lpus20", evaluation(“Lpus20Exact”), evaluation(“Lpus20SOA”),
derivative(wrt(”betai", ”alpha")) ),
realization(“qdp”, evaluation(“qdpExact”), evaluation(“qdpSOA”),
objectiveVars(var(”DIo", “DI", Target.min )),
constraintVars(var(”Ltotc", ”Ltot", Relation.eq, 1000.),
);

## Slide 179
AVUS_OUTPUT_OBJECT
ContextFilter(“AVUS/AVUSOUTPUT”)
ObjectFilter(“windAxisLpus”)
LPUS_ARRAY
LPUS_i
ListFilter(i)

## Slide 180
Functionally we see that and which can be written as
.
This is the functional composition to be represented in SORCER. is the dynamic pressure derived from the free stream velocity and the fluid density . The SORCER computing environment is depicted in. For the current discussion we will focus on the development of the Model aspect of this figure

## Slide 181
As can be seen in SORCER Models consists of three components, Variables, Evaluators, and Filters. The purpose of this example is to take the engineering functional realationship defined in and create a Model in SORCER. Currently SORCER has three types of models, ResponseModel, ParametricModel, and SensitivityModel. In the near future an OptimizationModel will be incorporated as well. Here we will show the development of each of the three available models. First, the development of a ResponseModel will be demonstrated. This will require the definition of the Model, the Variables, and then the configuration of the Variables with the appropriate Filters and Evaluators.
For the case depicted in there are a total of 21 design variables, 20 design variables associated with and one design variable associated with . The remaining control surface varibles will be “linked” (a set relationship) to . The response variables consists of the 20 lift per unit span values, , and the induced drag, . The primary classes that are used to develop the model can be found in the engineering.avus.requestor and engineering.avus.provider packages. The class names are AvusModeler.java and AvusModelConfigurator.java, InducedDrag.java, and AvusOutput.java.
Below are the significant statements and steps required to build the model.

## Slide 182
Define the Model and Variables - This can be done in one step with the following functional composition syntax.
ResponseModel avusRM = responseModel("Induced Drag Response Analysis",
designVars("cs",20),
designVars("alpha"),
linkedVars("cs", 20,21),
responseVars("lpus", 20),
responseVars("iDrag"));
This is a function with embeded statements. An instance of ResponseModel is created called avusRM, the name of the model is “Induced Drag Response Analysis”. This name is arbitrary and user specified. The next argument in the constructor is
DesignVars("cs",20) - Returns a list of 20 Variable objects with the type attribute set to “DESIGN” and names “cs1”, “cs2”, ... “cs20”.
DesignVars("alpha") - Returns a single Variable object with type attribute of “DESIGN” and name “alpha”
LinkedVars("cs", 20,21) - Returns a list of 20 Variable objects with type attribute “DESIGN” and kind attribute of “LINKED” with names “cs21”, “cs22”, ...”cs40”
ResponseVars("lpus", 20)- Returns a list of 20 Variable objects with type attribute of “RESPONSE” with names “lpus1”, “lpus2”, ...”lpus20”
ResponseVars("iDrag")Returns a Variable object with type attribute of “RESPONSE” with name “iDrag”
A formal definition of the Variable class and some of its available attributes can be found in Appendix A.
2. The next step required is to configure the DesignVariables, LinkedVariables, and the ResposneVariables.
a. configure the Design Variables - Each indepenedent design variable consists of zero, one, or more Filters. For this case the independent design variables reside in two locations. The variables reside in an ascii text file( AVUS_Boundary_Condition.dat) and resides in a separate ascii text file (AVUS_Job.job). In order to have the ability to get and set the values in these files from anywhere on the network (we have no idea where avus may run) we need to create Filter objects and place them into the Variables. Filters take a larger entity and “filter” out a portion of that entity for either reading, writing or passing to another filter. Since we are working with ascii text files in this case we will create BasicFileFilter objects (a list of the all currently available Filter types can be found in the sorcer.vfe.filter package) . Each BasicFileFilter requires a Pattern object which is used to locate the desired quantity in the entity. Here our pattern is essentially line, field, delimeter information. Other patterns such as regular expressions are available as well. Below is an excerpt from the AVUS_Boundary_Condition.dat file and the AVUS_Job.job file(the line numbers are not actually in the file. They are shown here to indicate where in the file the excerpt has been taken from).

## Slide 183: Modified One Point Approximation (MOA)
Apply SOA to the lift per unit span Fi not to DI

## Slide 184: Kriging Approximation
Is a generalized regression model (often chosen as a constant in practice)
Are a set of chosen basis functions
Are found by solving
(least squares if R is identity)
Is a correlation matrix
Vector of known responses at random sampling points

## Slide 185: Kriging Approximation
is one realization of a Gaussian process with mean of zero, variance , and a covariance that satisfies
(Gaussian correlation function)
(Cubic Spline correlation function)
Is the correlation function. Two considered in this work are

## Slide 186: SORCER is a Service-Object-Oriented Architecture
A service-oriented product development environment
  Provides an open flexible design environment which allows universal availability and incorporation of existing data, tools/methods, processes and hardware as services.
  Provides a common way to model your analysis and design process in conjunction with your product data.
A network-based distributed framework
  Supports collaboration among geographically distributed engineering and business partners.
SORCER Philosophy – Accessibility, Flexibility & Reusability
SORCER is Research Code!

## Slide 187: Service Oriented Computing EnviRonment - SORCER
SORCER is a programming and computing environment that enables one to perform large scale system level engineering analysis and design space exploration that may be in a distributed heterogeneous computing environment.
SORCER federates a series of Service Providers (which may be distributed) in real time and orchestrates the communication between the Service Providers based on a Control Strategy algorithm defined in an Exertion(process definition) to perform a multi-disciplinary analysis and or design space exploration.
A service-oriented product development environment

## Slide 188
Service
Proxy Object
Service
Registry
Mobile
Proxy
Object
Service
Provider
Requestor
Discovery & Register
Discovery & Lookup
Neutrality:
Location
Protocol
Implementation
A network-based distributed framework
Service Oriented
Service Oriented Computing EnviRonment - SORCER

## Slide 189: SORCER Paradigm
EO Programming
SORCER meta-OS
Metaprocessor
(Services)
Service Context
Signatures
Control Context
Filters
Evaluators
Variables
Metacomputer
Exertions
Models
Service Context
Service Types
Providers
Programming Env
OS
Processor
Computers
Implementation

## Slide 190: SORCER Terminology
Service provider : a remote object accepting exertions from service requestors and performs calculations. Can provider one or more services.
The grid: a collection of service providers on the network.
Exertion (think process representation or workflow): defines collaborations - service-oriented programs. An object that represents a process by specifying the relationship between services and the information passed between them.

## Slide 191: Service Providers
Wrap existing applications with java to expose one or more functionalities(services) of the application to the SORCER Environment
Public class xxxProvider extends ServiceProvider implements xxxRemoteInterface, SorcerConstants{ }
Tight integration with c, c++, fortran etc.. using jna, jni and swig. Allows interaction at the api level not at the file level. More efficient and robust.
Robustness & Reuse
Your Computational Environment is only as good as your Wrapping!

## Slide 192: Exertion
Elementary Exertion
Composite Exertion
Job
.
.
.
Job
Engineering Example
All are Objects

## Slide 193: SORCER Paradigm
EO Programming
SORCER meta-OS
Metaprocessor
(Services)
Service Context
Signatures
Control Context
Filters
Evaluators
Variables
Metacomputer
Exertions
Models
Service Context
Service Types
Providers
Programming Env
OS
Processor
Computers
Implementation

## Slide 194: Variable, Evaluator, Filter (VEF) Design Patterns
Lazy variable evaluation
  getValue vs. evaluate (demand driven calculations)
Evaluator – Decorator pattern
  Evaluator: getValue/evaluate implements EvaluationManagement
  Outer evaluator calls on its inner one
  Evaluator is observable and observer (functional programming)
Observer-Observable
  setChanged
  notify/update
Notes: Function composition is a very powerful way of reusing code and building programs from pieces.
Object composition provides good support for building software from pieces.
Building complete partial results can be a waste of resources, as the next function in the composition chain may need only a few first elements from the partial result variable list, so computing the rest of the list would be a waste of time.
A variable is a generator that, on request (getValue), provides a response-object.

## Slide 195: Evaluators
Evaluators – are used to determine the value of variables and their partial derivatives(chain rule works) with respect to their dependencies (Variables). Evaluators do not necessarily produce a scalar value. The result can be an entire database or file. (for a given set of input an application creates many outputs)
  Current Evaluator Types – ModelEvaluator, ExertionEvaluator, ExpressionEvaluator, GroovyEvaluator, JepEvaluator, MethodEvaluator, SOAEvaluator, FDEvaluator

## Slide 196: Filters
Filters - are used to map the results of Evaluators to Variable Values. Think unix shell piping. Filters take the output of Evaluators and reduce it to a single scalar value necessary to define a Variable value. Filters can be concatenated n times.
  Current Filter Types – BasicFileFilter, ContextFilter, FileFilter, GrepFilter, ListFilter, MapFilter, ObjetFilter, PatternFilter, TextFilter

## Slide 197: Objective Function, Constraints and Sensitivities
Objective Sensitivities:
Constraints Sensitivities:

## Slide 198: Modified One Point Approximation (MOA)
Apply SOA to the lift per unit span Fi not to DI

## Slide 199: Kriging Approximation
Is a generalized regression model (often chosen as a constant in practice)
Are a set of chosen basis functions
Are found by solving
(least squares if R is identity)
Is a correlation matrix
Vector of known responses at random sampling points

## Slide 200: Kriging Approximation
is one realization of a Gaussian process with mean of zero, variance , and a covariance that satisfies
(Gaussian correlation function)
(Cubic Spline correlation function)
Is the correlation function. Two considered in this work are

## Slide 201: Modified One Point Approximation (MOA)
Apply SOA to the lift per unit span Fi not to DI

## Slide 202: Kriging Approximation
Is a generalized regression model (often chosen as a constant in practice)
Are a set of chosen basis functions
Are found by solving
(least squares if R is identity)
Is a correlation matrix
Vector of known responses at random sampling points

## Slide 203: Kriging Approximation
is one realization of a Gaussian process with mean of zero, variance , and a covariance that satisfies
(Gaussian correlation function)
(Cubic Spline correlation function)
Is the correlation function. Two considered in this work are

## Slide 204: SORCER is a Service-Object-Oriented Architecture
A service-oriented product development environment
  Provides an open flexible design environment which allows universal availability and incorporation of existing data, tools/methods, processes and hardware as services.
  Provides a common way to model your analysis and design process in conjunction with your product data.
A network-based distributed framework
  Supports collaboration among geographically distributed engineering and business partners.
SORCER Philosophy – Accessibility, Flexibility & Reusability

## Slide 205: Service Oriented Computing EnviRonment - SORCER
SORCER is a programming and computing environment that enables one to perform large scale system level engineering analysis and design space exploration that may be in a distributed heterogeneous computing environment.
SORCER federates a series of Service Providers (which may be distributed) in real time and orchestrates the communication between the Service Providers based on a Control Strategy algorithm defined in an Exertion(process definition) to perform a multi-disciplinary analysis and or design space exploration.
A service-oriented product development environment