## Slide 1: Efficient Supersonic Air Vehicle Analysis and Optimization using SORCER
Scott A. Burton
American Optimization LLC
Air Force Research Laboratory
Aerospace Systems
Edward Alyanak and Raymond Kolonay
Air Force Research Laboratory
Aerospace Systems
Mike Sobolewski
Air Force Research Laboratory
Aerospace Systems
September 5, 2013
20th ISPE International Conference on Concurrent Engineering 2013
Public Release: 88ABW-2012-0598

## Slide 2: Outline
Introduction
ESAV
  Multidisciplinary Analysis (MDA) and N2 Diagram
  SORCER AirVehicle Provider and ESAV Model
  Optimization problem and algorithm
  Demo
  Results
Closing Remarks

## Slide 3: Introduction
MSTC and 6th Generation Fighter
  Physics-based analyses
  Integrated MDA
  Multidisciplinary optimization (MDO) algorithms
  Process integration and design optimization software: SORCER
ESAV Baseline
  Small, single engine fighter
  ~30k lb TOGW
  ~25k lb thrust engine
ESAV MDA in SORCER
  Geometry generation
  Aerodynamics
  Aeroelasticity
  Structural mechanics
  Performance
Notes: The ESAV MDA involves many analysis codes, which are integrated using SORCER.

## Slide 4
Geometry
(MSTCGEOM)
Wave Drag
(AWAVE)
Aeroelasticity (ASTROS)
Performance (MSTCPERF)
Area, Taper Ratio,
& Aspect Ratio
Range & Weight
Viscous & Profile Drag (FRICTION)
Subsonic Induced Drag (TORNADO)
Supersonic Induced Drag (WINGDES)
Notes: This is the ESAV N-squared analysis diagram.

## Slide 5
Geometry
(MSTCGEOM)
Wave Drag
(AWAVE)
Aeroelasticity (ASTROS)
Performance (MSTCPERF)
Area, Taper Ratio,
& Aspect Ratio
Range & Weight
Viscous & Profile Drag (FRICTION)
Subsonic Induced Drag (TORNADO)
Supersonic Induced Drag (WINGDES)
Notes: This is the ESAV N-squared analysis diagram.

## Slide 6
Geometry
(MSTCGEOM)
Wave Drag
(AWAVE)
Aeroelasticity (ASTROS)
Performance (MSTCPERF)
Area, Taper Ratio,
& Aspect Ratio
Range & Weight
Viscous & Profile Drag (FRICTION)
Subsonic Induced Drag (TORNADO)
Supersonic Induced Drag (WINGDES)
aeroelasticity
aerodynamics
aerodynamics
aerodynamics
aerodynamics
performance
geometry
weight
range
Skin, ribs and spars structural sizing optimization
Notes: Thing to note here is that there are 7 engineering analysis codes which include:
geometry generation, aerodynamic, aeroelastic, and performance analysis;
Four maneuver load cases for ASTROS structural sizing optimization: 9g pull at Mach 0.9; 7.2g pull at Mach 1.2; 3g push at Mach 1.2; and anti-symmetric 100 deg/s aileron roll at Mach 1.2.
~10 min per analysis
A SORCER Provider is used to supply engineering analyses via SORCER services.

## Slide 7
Geometry
(MSTCGEOM)
Wave Drag
(AWAVE)
Aeroelasticity (ASTROS)
Performance (MSTCPERF)
Area, Taper Ratio,
& Aspect Ratio
Range & Weight
Viscous & Profile Drag (FRICTION)
Subsonic Induced Drag (TORNADO)
Supersonic Induced Drag (WINGDES)
~10 min per MDA

## Slide 8
Area, Taper Ratio,
& Aspect Ratio
Range & Weight
Geometry
(MSTCGEOM)
Wave Drag
(AWAVE)
Aeroelasticity (ASTROS)
Performance (MSTCPERF)
Viscous & Profile Drag (FRICTION)
Subsonic Induced Drag (TORNADO)
Supersonic Induced Drag (WINGDES)
SORCER ESAV Entities
Geometry
(MSTCGEOM)
Wave Drag
(AWAVE)
Aeroelasticity (ASTROS)
Performance (MSTCPERF)
Viscous & Profile Drag (FRICTION)
Subsonic Induced Drag (TORNADO)
Supersonic Induced Drag (WINGDES)
Notes: The N2 diagram is implemented in SORCER via two primary entities: the Service Provider and the Model.

## Slide 9
SORCER ESAV Entities
Geometry
(MSTCGEOM)
Wave Drag
(AWAVE)
Aeroelasticity (ASTROS)
Performance (MSTCPERF)
Viscous & Profile Drag (FRICTION)
Subsonic Induced Drag (TORNADO)
Supersonic Induced Drag (WINGDES)
Area, Taper Ratio,
& Aspect Ratio
Range & Weight
Geometry
(MSTCGEOM)
Wave Drag
(AWAVE)
Aeroelasticity (ASTROS)
Performance (MSTCPERF)
Viscous & Profile Drag (FRICTION)
Subsonic Induced Drag (TORNADO)
Supersonic Induced Drag (WINGDES)
AirVehicle Provider
Engineering ESAV Model

## Slide 10
SORCER ESAV Entities
Geometry
(MSTCGEOM)
Wave Drag
(AWAVE)
Aeroelasticity (ASTROS)
Performance (MSTCPERF)
Viscous & Profile Drag (FRICTION)
Subsonic Induced Drag (TORNADO)
Supersonic Induced Drag (WINGDES)
Area, Taper Ratio,
& Aspect Ratio
Range & Weight
Geometry
(MSTCGEOM)
Wave Drag
(AWAVE)
Aeroelasticity (ASTROS)
Performance (MSTCPERF)
Viscous & Profile Drag (FRICTION)
Subsonic Induced Drag (TORNADO)
Supersonic Induced Drag (WINGDES)
AirVehicle Provider
Engineering ESAV Model
independent vars
dependent vars

## Slide 11
SORCER ESAV Entities
Geometry
(MSTCGEOM)
Wave Drag
(AWAVE)
Aeroelasticity (ASTROS)
Performance (MSTCPERF)
Viscous & Profile Drag (FRICTION)
Subsonic Induced Drag (TORNADO)
Supersonic Induced Drag (WINGDES)
Area, Taper Ratio,
& Aspect Ratio
Range & Weight
Geometry
(MSTCGEOM)
Wave Drag
(AWAVE)
Aeroelasticity (ASTROS)
Performance (MSTCPERF)
Viscous & Profile Drag (FRICTION)
Subsonic Induced Drag (TORNADO)
Supersonic Induced Drag (WINGDES)
AirVehicle Provider
Engineering ESAV Model
service operations
Several AirVehicle Providers are published on different computers to do parallel Space Computing...
Notes: The linking of each physics-based analysis and data flow are implemented in a SORCER Model.
All the physics-based analyses required for the ESAV MDA are implemented in a single SORCER Provider called the AirVehicle Provider.
Each blue box represents a Java-wrapped native executable required of the ESAV MDA and is referred to as a service operation.

## Slide 12: SORCER Space Computing
Parallel grid computing via JavaSpaces technology
  Space is published as a provider
  Space is repository for tasks
  Providers watch space for tasks with their service type
  Tasks are dropped into space by clients
  Providers pick-up, process, and return completed tasks to space
  Clients retrieve completed tasks
SORCER Space computing is a reliable, dynamically scalable, self-load balancing, distributed computing system.

## Slide 13
network
JavaSpace
Engineering Air Vehicle Provider
worker threads
Engineering Air Vehicle Provider
worker thread
Engineering Air Vehicle Provider
worker threads
Matlab Client
Engineering ESAV Model Provider
…
Independent
var: area
MSTCPERF task
var: range

## Slide 14
JavaSpace
network
Engineering Air Vehicle Provider
worker threads
Engineering Air Vehicle Provider
worker thread
Engineering Air Vehicle Provider
worker threads
Engineering ESAV Model Provider
…
Independent
var: area
MSTCPERF task
var: range
[X]
Matlab Client
new models for parallel table execution

## Slide 15
JavaSpace
network
Engineering Air Vehicle Provider
worker threads
Engineering Air Vehicle Provider
worker thread
Engineering Air Vehicle Provider
worker threads
Engineering ESAV Model Provider
…
Independent
var: area
MSTCPERF task
var: range
[X]
new models for parallel table execution
[X Y]
Matlab Client

## Slide 16: ESAV SORCER Demo
Wing Optimization Problem
  Minimize weight
  Design variables
    Wing area
    Aspect ratio
    Structural sizing properties
  One constraint
    1400 mi range minimum
  Robust successive linear programming (SLP) algorithm
Notes: Range is calculated for an optimal altitude trajectory.

## Slide 17: DEMO
Notes: Range is calculated for an optimal altitude trajectory.

## Slide 18: ESAV SORCER Demo
Robust SLP Algorithm
  First-things first: Parameter studies
    Vet MDA
    Finite-difference step sizes
    SLP move limits
  Gradient calculations
    High-order central differences
    Parallel
  Linear programming solution subject to move limits
  Line search, sort of
    Partial enumeration of line
    Parallel
  Visual feedback
Dobjective
ALPHA = 0%
ALPHA = 100%
linear model prediction
actual results
LP solution
x1
x2
Notes: Range is calculated for an optimal altitude trajectory.

## Slide 19: ESAV SORCER Example
Wing Optimization Problem
  Minimize weight
  Subject to minimum range
    6000 lb fuel burn @ Mach 0.8
  Design variables
    Wing area
    Aspect ratio
    Taper ratio
    Structural sizing properties
  Comments
    Case 1: 1500 mi range minimum
    Case 2: 2500 mi range minimum
    Robust SLP algorithm
    Three Linux boxes and two Macs
Notes: Range is calculated for an optimal altitude trajectory.

## Slide 22: Closing Remarks
SLP optimization method
  Worked…failure tolerance was critical
SORCER software
  Results consistent with expectations; provider implementations sound
  Space computing worked well
    Increased throughput 5x
    Allowed for dynamic addition/subtraction of computers for parallel execution
Thank You.

## Slide 23
network
Java Virtual Machine Process
Engineering Air Vehicle Provider
doMstcGeomService
executeAwave
IndependentEvaluator
evaluator value
ExpressionEvaluator
evaluator value
expr: “X1 + X2”
vars: x1, x2

## Slide 24: SORCER Overview
SORCER Tasks
  Client-side object to use remote services
  Contains
    Signature
      Service type
      Service
      Provider name (optional)
    Context
  Client calls method on task to execute
Task
Context
Signature
Tasks use remote services to do calculations; Evaluators do local and remote.
Engineering Air Vehicle Provider
doMstcGeomService
executeAwave

## Slide 25
Engineering Air Vehicle Provider
worker threads
network
Matlab Client
Engineering ESAV Model Provider
new models for parallel table execution
Engineering Air Vehicle Provider
worker thread
Engineering Air Vehicle Provider
worker threads
JavaSpace
[X]
[X Y]
…
Independent
var: area
MSTCPERF task
var: range

## Slide 26
analysis provider thread takes tasks for its worker threads; when work is done, puts back into space
matlab submits table to model via Java method
Engineering Air Vehicle Provider
worker threads
network
models writing/taking tasks to/from space
Matlab Client
Engineering ESAV Model Provider
new models for parallel table execution
Engineering Air Vehicle Provider
worker thread
Engineering Air Vehicle Provider
worker threads
JavaSpace
[X]
[X Y]
…
Independent
var: area
MSTCPERF task
var: range

## Slide 27: SORCER ESAV Implementation
ESAV MDA - SORCER Air Vehicle Provider
  All services are available in one provider
ESAV MDA Model
  Xs: wing design variables
  Ys: range and weight
ESAV MDO - Matlab
  Objective & constraints via SORCER ModelClient
Notes
  SORCER can drive or be driven
  SORCER clients can be Java, command-line, or shell script

## Slide 28
range
range

## Slide 29
Geometry
(MSTCGEOM)
Wave Drag
(AWAVE)
Aeroelasticity (ASTROS)
Performance (MSTCPERF)
Area, Taper Ratio,
& Aspect Ratio
Range & Weight
Viscous & Profile Drag (FRICTION)
Subsonic Induced Drag (TORNADO)
Supersonic Induced Drag (WINGDES)
aeroelasticity
aerodynamics
aerodynamics
aerodynamics
aerodynamics
performance
geometry
Notes: Thing to note here is that there are 7 engineering analysis codes which include:
geometry generation, aerodynamic, aeroelastic, and performance analysis;
Four maneuver load cases for ASTROS structural sizing optimization: 9g pull at Mach 0.9; 7.2g pull at Mach 1.2; 3g push at Mach 1.2; and anti-symmetric 100 deg/s aileron roll at Mach 1.2.
~10 min per analysis
A SORCER Provider is used to supply engineering analyses via SORCER services.

## Slide 30
ESAV Analysis via Space Computing Demo
Geometry
(MSTCGEOM)
Wave Drag
(AWAVE)
Aeroelasticity (ASTROS)
Performance (MSTCPERF)
Viscous & Profile Drag (FRICTION)
Subsonic Induced Drag (TORNADO)
Supersonic Induced Drag (WINGDES)
Area, Taper Ratio,
& Aspect Ratio
Range & Weight
Geometry
(MSTCGEOM)
Wave Drag
(AWAVE)
Aeroelasticity (ASTROS)
Performance (MSTCPERF)
Viscous & Profile Drag (FRICTION)
Subsonic Induced Drag (TORNADO)
Supersonic Induced Drag (WINGDES)
AirVehicle Provider
Engineering ESAV Model
independent vars
dependent vars
intermediate vars
service type & operation

## Slide 31: Introduction and Background
SORCER (Service-Oriented Computing Environment)
  Java-based code developed at AFRL
  Service-oriented
    Open flexible design
    Allows the incorporation of existing methods and data as services
    Provides a common way to model analyses and design processes
  Network-based, distributed framework
    Services are discovered with Java Jini technology
    Supports collaboration among geographically distributed engineering and business partners
    Supports parallel computing via JavaSpaces technology
Notes: SORCER is used at AFRL MSTC for ESAV studies.

## Slide 32
LP Example

## Slide 33
DV Sweep

## Slide 34
Gradient

## Slide 35
Gradient

## Slide 36
DV Bounds
DV Bounds

## Slide 37
DV Bounds

## Slide 38
LP Solution

## Slide 39
LP Solution

## Slide 40
Line Search
ALPHA = 0%
ALPHA = 100%

## Slide 41
Line Search

## Slide 42
Line Search
DCFG [%]
ALPHA = 0%
ALPHA = 100%
linear model prediction
CFX results

## Slide 43: Introduction and Background
Air Force Research Lab’s (AFRL) Multidisciplinary Science and Technology Center (MSTC)
  Efficient supersonic air vehicle (ESAV)
    Next generation fighter
  Research areas
    Multidisciplinary analysis
    Multidisciplinary optimization
    Design processes and software
The conceptual design process is key in obtaining performance and affordability.
Notes: The conceptual design process is key in obtaining performance and affordability.

## Slide 44: Introduction and Background
Conceptual design (CD)
  Determines most of air vehicle cost
  Many configurations analyzed
  Low fidelity tools
    Closed-form equations
    Statistical models
  Higher fidelity CD
    Increased computational expense
    Increased number of engineering analysis codes
    Increased complexity in process integration
Need conceptual design process to handle higher fidelity analyses…SORCER.
Notes: Low fidelity tools can miss critical physics
Need conceptual design process to handle higher fidelity analyses…SORCER.

## Slide 45
Java methods
  Engineering analyses
  Context in, Context out
SORCER Services
AirVehicleInterface
Context doMstcGeomService(Context ctx);
Context executeAwave(Context ctx);
argument type
return value type

## Slide 46
Engineering Air Vehicle Provider
(AirVehicleInterface)
doMstcGeomService
executeAwave
Java methods
  Engineering analyses
  Context in, Context out
SORCER Services
argument
Context
  Key-value pairs
  Keys define namespace
  Values have SORCER data type attribute
  Value
    Any Java object (e.g., URL)
    Provider-specific objects
input_1http://input.txt [type.mstcg.input]
key
value
[data type]
context
input_1http://input.txt [type.mstcg.input]
output_1http://output.txt [type.astros.input]
return value
Notes: Services like doMstcGeomService and executeAwave are typically not all Java code.

## Slide 47: SORCER Vars
SORCER Filter
  Operates on value returned from evaluator
  Reduces or transforms
SORCER Persisters
  Operates on value returned from filter
  Sets value
    Writes file
    Passes to object
file
Var: y1
filter
evaluator reference
y1 value
evaluator value
persister
ExertionEvaluator
Task
Context
Signature
evaluator value
file
Var: y2
filter
evaluator reference
y2 value
evaluator value
persister
Notes: Filters may be chained together to for a filter pipeline.

## Slide 48: SORCER Provider
Java object in a JVM on a computer
Provide Java methods called service operations to remote users over a network
Implements a Java interface called a service type
AirVehicleInterface
Context doMstcGeomService(Context ctx);
Context executeAwave(Context ctx);
service type
service ops
provider object
provider name
service ops
JVM Process
Engineering Air Vehicle Provider
(AirVehicleInterface)
doMstcGeomService
executeAwave
service type
Notes: Users don’t need to know where a provider is, nor it’s name (no host, port, or name required)

## Slide 49: SORCER Service Operations
Typically wrap engineering analysis executables
Java service code may augment native executables
Communication
  File-based
  Java Native Interface (JNI)
  Java Native Access (JNA)
Engineering Air Vehicle Provider
doMstcGeomService
executeAwave
awave.exe
executes
reads
writes
output file
reads
writes
input file
Notes: SORCER services are used by clients via the Evaluator object.

## Slide 50: SORCER Evaluators
Client-side object to perform calculations
ExertionEvaluator
  Use remote services
  Require Task object
    Service type
    Service op
    Provider name (optional)
    Context (service op argument)
provider name
service ops
Engineering Air Vehicle Provider
(AirVehicleInterface)
doMstcGeomService
executeAwave
service type
ExertionEvaluator
Task
Context
Signature
evaluator value
provider name
(optional)
service op
service type
ExertionEvaluators typically produce aggregate forms of data.
Notes: Evaluators are used in SORCER Vars to create mathematical functions…

## Slide 51: SORCER Vars
Mathematics
  Independent variables
  Functions
  Composite functions
Demand-driven
Multi-fidelity
Objects in Vars
  Evaluator
  Filter
  Persister
Var: y1v
evaluator reference
y1v value
evaluator value
ExertionEvaluator
Task
Context
Signature
evaluator value
ExertionEvaluator
Task
Context
Signature
evaluator value
ExertionEvaluator
Task
Context
Signature
evaluator value
ExertionEvaluator
Task
Context
Signature
evaluator value
multi-fidelity

## Slide 52: SORCER Models
Collection of vars
May be published as a provider
Single model query
  Set Xs, get Ys
  Behaves like shared memory
Table model query
  Rows of Xs
  Creates new isolated model objects
  Executes in parallel
OptimizationModel: model1
Var: y1v
filter
Var: x1v
Var: y2v